## Slide 1: Lecture 2 Supplement Verilog-01
Based on
Fundamentals of Digital Logic with Verilog Design
By Brown/Vranesic 3rd.
Chung-Ho Chen

## Slide 2: Describe a circuit in a form of module Gate Level
module mux (x1, x2, s, f);
input x1, x2, s;
output f;
not (si,s);
and (u, si, x1);
and (l, s, x2);
or (f, u, l);
endmodule
output
keyword
and (u, ~s, x1); // without an explicit not ahead

## Slide 3: Behavioral: logic equation
module mux (x1, x2, s, f);
input x1, x2, s;
output f;
assign f = (~s & x1) | (s &x2);
assign y = f | x2;
endmodule
Continuous assignment:
f is re-evaluated whenever
the right hand side
signal changes.
No order for f and y,
concurrent statement;
assign: for nets (like wire) since nets can not
hold values, so you need to assign the
value continuously.

## Slide 4: Behavioral: procedural statement
module mux (x1, x2, s, f);
input x1, x2, s;
output f;
reg f;
always@(x1 or x2 or s)
if (s == 0)
f = x1;
else
f = x2;
endmodule
always@(sensitivity list)
Evaluated in the order
given by the code;
if first, then else.
= blocking assignment
(evaluated in order)

## Slide 5: Coding in 3 ways:
Gate instantiation
Continuous assignment (assign)
Procedural statements (always)
  Blocking assignment = sequencing
    S = X + Y;
    C = S[0]; // C takes the new value from X+Y.
  Non-blocking assignment <=
    S <= X + Y;
    C <= S[0]; // at simulation time ti, C takes the value of S[0] at simulation time ti-1

## Slide 6: More compact procedural statement
module mux (input x1, x2, s, output reg f);
always@(x1, x2,s)
if (s == 0)
f = x1;
else
f = x2;
endmodule

## Slide 7: Hierarchical Verilog Code
X1
X2
A
B
C
D
E
a
b
c
d
y1
y2
a
b
c
d
e
module front (a, b, c, d);
Input a, b;
output c, d;
…..
endmodule
module back (y1, y2, a, b, c, d, e);
Input y1, y2;
output a, b, c, d, e;
…..
endmodule
w0
w1
module whole (X1, X2, A, B, C, D, E);
Input X1, X2;
output A, B, C, D, E;
wire w0, w1;
front U1 (X1, X2, w0, w1);
back U2 (w0, w1, A, B, C, D, E);
…..
endmodule
Top-level module
Internal (not output or input) uses wire.

## Slide 8: Full Adder Using Gates
module fulladd (Cin, x, y, s, Cout);
input Cin, x, y;
output s, Cout;
xor (s, x, y, Cin);
and (a, x, y);
and (b, x, Cin);
and (c, y, Cin);
or (Cout, a, b, c);
endmodule
module fulladd (Cin, x, y, s, Cout);
input Cin, x, y;
output s, Cout;
xor (s, x, y, Cin);
and (a, x, y),
(b, x, Cin), //omit and
(c, y, Cin);
or (Cout, a, b, c);
endmodule

## Slide 9: Full Adder Using Functional Expression
module fulladd (Cin, x, y, s, Cout);
input Cin, x, y;
output s, Cout;
assign s = x ^ y ^ Cin,
Cout = (x & y) | (x & Cin) | (y & Cin);
endmodule

## Slide 10: 3-bit Ripple Adders
module adder3 (c0, x2, x1, x0, y2, y1, y0, s2, s1, s0, carryout);
input c0, x2, x1, x0, y2, y1, y0;
output s2, s1, s0, carryout;
fulladd b0 (c0, x0, y0, s0, c1);
fulladd b1 (c1, x1, y1, s1, c2);
fulladd b2 (c2, x2, y2, s2, carryout);
endmodule
module fulladd (Cin, x, y, s, Cout);
input Cin, x, y;
output s, Cout;
assign s = x ^ y ^ Cin,
assign Cout = (x & y) | (x & Cin) | (y & Cin);
endmodule
Instantiate the
fulladd module

## Slide 11: 3-bit Ripple Adders Using Vectored Signals
module adder3 (c0, x2, x1, x0, y2, y1, y0, s2, s1, s0, carryout);
input c0, x2, x1, x0, y2, y1, y0;
output s2, s1, s0, carryout;
fulladd b0 (c0, x0, y0, s0, c1);
fulladd b1 (c1, x1, y1, s1, c2);
fulladd b2 (c2, x2, y2, s2, carryout);
endmodule
module fulladd (Cin, x, y, s, Cout);
input Cin, x, y;
output s, Cout;
assign s = x ^ y ^ Cin,
assign Cout = (x & y) | (x & Cin) | (y & Cin);
endmodule
module adder3 (c0, X, Y, S, carryout);
input c0;
input [2:0] X, Y;
output [2:0] S;
output carryout;
wire [2:1] C;
fulladd b0 (c0, X[0], Y[0], S[0], C[1]);
fulladd b1 (C[1], X[1], Y[1], S[1], C[2]);
fulladd b2 (C[2], X[2], Y[2], S[2], carryout);
endmodule
Vectored signals used

## Slide 12: n-bit Ripple Adders
module adderN (c0, X, Y, S, carryout);
parameter n = 16;
input c0;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout;
reg [n:0] C;
integer k;
always @(X, Y, c0)
begin
C[0] = c0;
for (k = 0; k < n; k = k+1)
begin
S[k] = X[k] ^ Y[k] ^ C[k];
C[k+1] = (X[k] & Y[k]) | (X[k] & C[k]) | (Y[k] & C[k]);
end
carryout = C[n];
end
endmodule
1: for: a procedural statement, must be inside a always block
2: Values inside a always block must retain their values until any change of signals in the sensitivity list. To hold on the values, use reg to keep them.
There is no physical meaning of k in the circuit.
It is used to tell the compiler that how
many instances of the iteration are needed.

## Slide 13: 3-bit to n-bit transformation using generate
module adder3 (c0, X, Y, S, carryout);
input c0;
input [2:0] X, Y;
output [2:0] S;
output carryout;
wire [2:1] C;
fulladd b0 (c0, X[0], Y[0], S[0], C[1]);
fulladd b1 (C[1], X[1], Y[1], S[1], C[2]);
fulladd b2 (C[2], X[2], Y[2], S[2], carryout);
endmodule
module addern (c0, X, Y, S, carryout);
parameter n = 16;
input c0;
input [n-1:0] X, Y;
output [n-1:0] S;
output carryout;
wire [n:0] C;
genvar i; // to be used in generate
assign C[0] = c0;
assign carryout = C[n];
generate
for (i = 0; i <= n-1; i = i+1)
begin:adderbit
fulladd b (C[i], X[i], Y[i], S[i], C[i+1]);
end
endgenerate
endmodule
Instantiate a submodule n times using
generate
Instance name produced
adderbit[0].b
adderbit[1].b
….
adderbit[15].b

## Slide 14: Overflow and Carry-Out detection
For unsigned number
carry out from n-1 bit position:
If both xn-1 and yn-1 are 1 or
If either xn-1 or yn-1 is 1 and sn-1 is 0.
Hence,
carryout = xn-1 yn-1 + ~sn-1 xn-1 + ~sn-1 yn-1
n-bit signed number: -2n-1 to 2n-1 -1
Detect overflow for signed number:
Overflow = Cn-1 ⊕ Cn
Overflow = Xn-1 Yn-1 ~Sn-1 (110) + ~Xn-1 ~Yn-1 Sn-1 (001)
(summation of two same signs produce different sign)
where X and Y represent the 2’s complement numbers, S = X+Y. (sign bits 0, 0 ≠ 1 )
0111
0111
1111

## Slide 15: n-bit adder with overflow and carryout
module addern (carryin, X, Y, S, carryout, overflow);
parameter n = 32;
input carryin;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout, overflow;
always @(X, Y, carryin)
begin
S = X + Y + carryin; // arithmetic assignment
carryout = (X[n-1] & Y[n-1]) | (X[n-1] & ~S[n-1]) | (Y[n-1] & ~S[n-1]);
overflow = (X[n-1] & Y[n-1] & ~S[n-1]) | (~X[n-1] & ~Y[n-1] & S[n-1]);
end
endmodule

## Slide 16: Another way to get carryout
module addern (carryin, X, Y, S, carryout, overflow);
parameter n = 32;
input carryin;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout, overflow;
reg [n:0] Sum; //n+1 bits, nth for the carryout
always @(X, Y, carryin)
begin
Sum = {1'b0,X} + {1'b0,Y} + carryin; // One 0 bit is concatenated (,) with X
S = Sum[n-1:0];
carryout = Sum[n];
overflow = (X[n-1] & Y[n-1] & ~S[n-1]) | (~X[n-1] & ~Y[n-1] & S[n-1]);
end
endmodule
Will this work?
Sum = X + Y + carryin;?

## Slide 17: Better
module addern (carryin, X, Y, S, carryout, overflow);
parameter n = 32;
input carryin;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout, overflow;
always @(X, Y, carryin)
begin
{carryout, S} = X + Y + carryin; //using concatenation
overflow = (X[n-1] & Y[n-1] & ~S[n-1]) | (~X[n-1] & ~Y[n-1] & S[n-1]);
end
endmodule

## Slide 18: Module Hierarchy in Verilog two adders: 16-bit and 8-bit
module addern (carryin, X, Y, S, carryout, overflow);
parameter n = 32;
input carryin;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout, overflow;
always @(X, Y, carryin)
begin
{carryout, S} = X + Y + carryin;
overflow = (X[n-1] & Y[n-1] & ~S[n-1]) | (~X[n-1] & ~Y[n-1] & S[n-1]);
end
endmodule
module adder_hier (A, B, C, D, S, T, overflow);
input [15:0] A, B;
input [7:0] C, D;
output [16:0] S;
output [8:0] T;
output overflow;
wire v1, v2; // used for the overflow signals
addern U1 (1’b0, A, B, S[15:0], S[16], v1);
defparam U1.n = 16;
addern U2 (1’b0, C, D, T[7:0], T[8], v2);
defparam U2.n = 8;
assign overflow = v1 | v2;
endmodule
defparam: define n to be 16
S[16] and T[8] for
unsigned carryout

## Slide 19: Specifying Parameters two adders: 16-bit and 8-bit
module adder_hier (A, B, C, D, S, T, overflow);
input [15:0] A, B;
input [7:0] C, D;
output [16:0] S;
output [8:0] T;
output overflow; // not in an always block
wire v1, v2; // used for the overflow signals
addern U1 (1’b0, A, B, S[15:0], S[16], v1);
defparam U1.n = 16;
addern U2 (1’b0, C, D, T[7:0], T[8], v2);
defparam U2.n = 8;
assign overflow = v1 | v2;
endmodule
addern #(16) U1 (1’b0, A, B, S[15:0], S[16], v1);
Using # operator.

## Slide 20: Named port connection
module addern (carryin, X, Y, S, carryout, overflow);
parameter n = 32;
input carryin;
input [n-1:0] X, Y;
output reg [n-1:0] S;
output reg carryout, overflow;
always @(X, Y, carryin)
begin
{carryout, S} = X + Y + carryin;
overflow = (X[n-1] & Y[n-1] & ~S[n-1]) | (~X[n-1] & ~Y[n-1] & S[n-1]);
end
endmodule
module adder_16(A, B, S, overflow);
input [15:0] A, B;
output [16:0] S;
output overflow; // not in an always block
wire v1; // used for the overflow signals
addern #(.n(16)) U1
(
.carryin(1’b0),
.X (A),
.Y (B),
.S (S[15:0),
.carryout (S[16]),
.overflow (v1)
);
assign overflow = v1;
endmodule

## Slide 21: So far, nets and variables
Net: connecting things.
  wire. A wire connects an output of one logic element to the input of another logic element. No need to declare scalar signals of wire, since signals are nets by default.
  tri. Another net is tri denoting circuit nodes which are connected in tri-state.
Variable: used to describe behaviors of the circuits.
  reg. reg does not denote a storage element or register. reg can model either combinational or sequential part of the circuit.
  integer.