## Slide 1: Supplement on Verilog for Algorithm State Machine Chart
Based on
Fundamentals of Digital Logic with Verilog Design
and Fundamental of Logic Design
Chung-Ho Chen

## Slide 2: Problem: Bit Counter
B
=
0
;
while
A

0
do
if
a
0
=
1
then
B
=
B
+
1
;
end if;
Right-shift
A
;
end while;
Count the number of 1s’ in A
And store the number of 1s in B

## Slide 3: ASM Chart for Bit Counter
B
=
0
;
while
A

0
do
if
a
0
=
1
then
B
=
B
+
1
;
end if;
Right-shift
A
;
end while;
s=1, start counting
Initialize B
Start another ?
Conditional output
S2 which performs the shift is actually shifted at
the next clock edge, so the checking of A, and a0 are
performed before the shift of A.
S1
Load B
S2
Shift A
Update B (a0=1)

## Slide 4: Datapath for the bit counter
A shift register
A counter register
Need to test if a0=1
Need test if A=0?
Need load/enable signals
If n = 8, need how many bits?
+1
+1
A <> 0?

## Slide 5: ASM Chart for Bit Counter to Verilog Code
s=1, start counting
LB
Start another ?
Conditional output
EA
Z
EB
module bitcount (Clock, Resetn, LA, s, Data, B, Done);
input Clock, Resetn, LA, s;
input [7:0] Data;
output reg [3:0] B;
output reg Done;
wire [7:0] A;
wire z;
reg [1:0] Y, y;
reg EA, EB, LB;
// control circuit
parameter S1 = 2'b00, S2 = 2'b01, S3 = 2'b10;
always @(s, y, z)
begin: State_table
case (y)
S1: if (!s) Y = S1;
else Y = S2;
S2: if (z == 0) Y = S2;
else Y = S3;
S3: if (s) Y = S3;
else Y = S1;
default: Y = 2'bxx;
endcase
end
always @(posedge Clock, negedge Resetn)
begin: State_flipflops
if (Resetn = = 0)
y <= S1;
else
y <= Y;
end
… continued in Part b.
y: PS
Y: NS

## Slide 6: ASM Chart for Bit Counter to Verilog Code
s=1, start counting
LB
Start another ?
Conditional output
EA
Z
EB
always @(y, A[0])
begin: FSM_outputs // Control data path
// defaults
EA = 0; LB = 0; EB = 0; Done = 0;
case (y)
S1: LB = 1;
S2: begin
EA = 1;
if (A[0]) EB = 1;
else EB = 0;
end
S3: Done = 1;
endcase
end
// datapath circuit
// counter B
always @(negedge Resetn, posedge Clock)
if (!Resetn)
B <= 0;
else if (LB)
B <= 0;
else if (EB)
B <= B + 1;
shiftrne ShiftA (Data, LA, EA, 0, Clock, A);
assign z = ~| A; // reduction NOR.
endmodule
Outputs in a state

## Slide 7: Shift Right Register
module shiftrne (R, L, E, w, Clock, Q);
parameter n = 4;
input [n-1:0] R;
input L, E, w, Clock;
output reg [n-1:0] Q;
integer k;
always @(posedge Clock)
begin
if (L)
Q <= R;
else if (E)
begin
Q[n-1] <= w;
for (k = n-2; k >= 0; k = k-1)
Q[k] <= Q[k+1];
end
end
endmodule