## Slide 1: Laboratory 10 PWM Breathing Light

## Slide 2: Purpose
熟悉 PYNQ-Z2 Board
了解 PWM (Pulse Width Modulation)

## Slide 3: Outline
Introduction to PYNQ-Z2
Introduction to PWM
Lab Problem
  Part 1 - Behavioral Simulation
  Part 2 - PYNQ Board Implementation

## Slide 4: Outline
Introduction to PYNQ-Z2
Introduction to PWM
Lab Problem
  Part 1 - Behavioral Simulation
  Part 2 - PYNQ Board Implementation

## Slide 5: FPGA (Field Programmable Gate Array)
前幾次Lab中我們所完成的Verilog電路，若要被製作成真的電路，還必須經過幾個步驟。
  邏輯合成(Logic Synthesis)，是將電路轉換為製造商可支援的標準元件(standard cell)型式。
  布局和布線(Place & Route)，將轉換完的元件擺放和排線。
現場可程式化邏輯閘陣列 (Field Programmable Gate Array, FPGA)，是由許多的Logic block和接點組成的電路，透過燒錄的方式改變接點的開關，將其轉變為我們設計的電路。
過去幾周Lab所使用的Vivado，除了可以模擬電路，
最主要的功能其實是將電路合成和PR後，
燒錄至FPGA。

## Slide 6: PYNQ-Z2 Board Connection Check
1. plug micro USB (Use USB port as power supply)
2. Turn on power switch
3. Connect to device
4. Check hardware panel
power switch
Hardware panel
Connect to device(Left down manual )
Plug-in USB
Set power mode to USB

## Slide 7: PYNQ Synthesis Procedure
Busy
Done
1
2
3
4
5
6
7
8

## Slide 8: Outline
Introduction to PYNQ-Z2
Introduction to PWM
Lab Problem
  Part 1 - Behavioral Simulation
  Part 2 - PYNQ Board Implementation

## Slide 9: Duty Cycle
Duty cycle : Ratio of cycle period is ON compared to the time is OFF
Period T

## Slide 10: Pulse Width Modulation
PWM is the mechanism of representing analog signals with digital signals by controlling the duty cycle of the periods.
Analog Signal : Continuous
Digital Signal : Discrete
Analog signal
Digital signal
Figure source : https://www.monolithicpower.com/en/analog-vs-digital-signal

## Slide 11: Pulse Width Modulation - Cont.
Digital signal ACTIVATE/OFF represents switch ON/OFF of the circuit, controlling the average current of each period
In general VL is zero; D is the duty; Vavg = D x VH
The average value of the signal is directly dependent on the duty cycle D

## Slide 12: Clock Divider - 1
Divide clock frequency by 2
div
trigger
n_rst

## Slide 13: Clock Divider - 2

## Slide 14: Ripple Counter
LSB
MSB
Cycle | dff5 | dff4 | dff3 | dff2 | dff1 | Value
1 | 0 | 0 | 0 | 0 | 0 | 0
2 | 0 | 0 | 0 | 0 | 1 | 1
3 | 0 | 0 | 0 | 1 | 0 | 2
4 | 0 | 0 | 0 | 1 | 1 | 3
5 | 0 | 0 | 1 | 0 | 0 | 4
6 | 0 | 0 | 1 | 0 | 1 | 5
dff 1
dff 5
dff 2
dff 3
dff 4
多個Clock Divider 串接，可以利用dff之間有著propagate的效果，將多個串接的dff視為一個counter；第一個的divider的output為LSB，而最後一個dff的output為MSB。

## Slide 15: PWM Implementation
Modulation Wave
Analog
Signal
Discrete
Sample
PWM
Signal
phase0
phase1
phase2
phase4
phase3
phase5
phase6
phase7
phase8
phase9
Wave
phase
phase_trig n+1
Duty = 50%
Duty = 25%
phase_trig n
phase_trig n+2
duty_trig
duty_trig

## Slide 16: Simple PWM
由於sysclk的頻率為125MHZ，請先嘗試以clock divider將頻率降至適合操作的頻率
當phase的週期小於人眼圖像滯留的時間(約為40ms)，可以減少燈光閃爍的現象
Duty 為每次phase trigger之後set high的cycles，下圖的一個phase有八個cycle，duty分別為4和2，因此兩個phase的duty ratio分別為50%和25%

## Slide 17: Simple PWM - Clock Divider
module ripple_div(
input rst,
input sysclk,
output wire [31:0] div
);
//Implement your code
endmodule

## Slide 18: Simple PWM - Phase Counter
module phase_counter(
input enable,
input [7:0] phase_shift,
input[31:0] div,
output wire duty_trig,
output wire phase_trig,
output wire [7:0] duty
);
//Implement your code
endmodule

## Slide 19: Simple PWM - 8 bit phase PWM
module pwm(
input rst,
input enable,
input duty_trig,
input phase_trig,
input [7:0] duty,
output wire out
);
reg[7:0] count;
assign out = ((count < duty) | phase_trig) & enable;
always@(posedge duty_trig or posedge rst)begin
if(rst)begin
count <= 8'b0;
end else if(phase_trig)begin
count <= 8'b0;
end else if(duty_trig)begin
count <= count + 1;
end else begin
count <= count;
end
end
endmodule

## Slide 20: Outline
Introduction to PYNQ-Z2
Introduction to PWM
Lab Problem
  Part 1 - Behavioral Simulation
  Part 2 - PYNQ Board Implementation

## Slide 21: Configurations
Behavioral Simulation
1. Disable top.v
2. Disable design_1_wrapper.v
3. Enable top_tb.v
4. Set top_tb.v as top
PYNQ Board Implementation
1. Disable top_tb.v
2. Enable top.v
3. Enable design_1_wrapper.v
4. Set design_1_wrapper.v as top

## Slide 22: I/O port of module
I/O port of module dff_div
I/O port of module ripple_div
Name | I/O | Width | Description
n_rst | Input | 1 | Active-low asynchronous reset signal
trigger | Input | 1 | Input clock
div | Output | 1 | Divided result
Name | I/O | Width | Description
n_rst | Input | 1 | Active-low asynchronous reset signal
sysclk | Input | 1 | System clock ( 125 MHZ )
div | Output | 32 | Divided result

## Slide 23: I/O port of module
I/O port of module phase counter
I/O port of module LUT_sin
Name | I/O | Width | Description
enable | Input | 1 | SW[0] ¦ SW[1] on FPGA board
phase_shift | Input | 8 | Offset of duty
div_clk | Input | 32 | Ripple Counter Result
duty_trig | Output | 1 | Trigger on every 256 cycles of sysclk
phase_trig | Output | 1 | Triggered when the startup of phase ( every 256 duty trig cycles )
duty | Output | 8 | Threshold of phase (Duty ratio)
Name | I/O | Width | Description
phase_idx | Input | 8 | Output of signal duty in phase counter
data | Output | 8 | Transform the threshold from linear to sine wave

## Slide 24: I/O port of module
I/O port of module pwm
Name | I/O | Width | Description
rst | Input | 1 | Active-high asynchronous reset signal
enable | Input | 1 | SW[0] ¦ SW[1] on FPGA board
duty_trig | Input | 1 | High every 256 cycles of sysclk
phase_trig | Input | 1 | High when the startup of phase ( every 256 duty trig cycles )
duty | Input | 8 | Threshold of phase
out | Output | 1 | Switch ON/OFF of led on FPGA board

## Slide 25: Behavioral Simulation - Problem 1
產生一組週期性的三角波，結報需解釋波型的產生方法與波型圖截圖(如下圖)。
右鍵 > Waveform Style > Analog

## Slide 26: Behavioral Simulation - Problem 2
請利用 LUT_sin module 產生一組正弦
結報需解釋波型的產生方法與波型圖截圖(如下圖)。

## Slide 27: PYNQ Implementation - Breathing Light
白光呼吸燈
混色光呼吸燈

## Slide 28: PYNQ Implementation - Breathing Light
實作top.v檔實作呼吸燈電路。可依需求修改 top檔案內非port name的部分(切記不可修改top.v 的port name，不然會合成失敗)。接著合成Bitstream檔並燒入到FPGA內。
Note : FPGA內LED4、LED5內有三種獨立RGB LED燈。可自行挑選。沒有使用的output線路記得要在top module內接地。(Assign to 0)。

## Slide 29: 本次結報需要附上的內容
Behavioral Simulation
  波形產生解釋和截圖波形
  實驗心得
PYNQ Board Implementation
  實驗心得(實作遇到什麼困難等等...)

## Slide 30: 本次結報注意事項
以 Lab10_Groupx 作為結報名稱
5/17 23:59 前於 moodle 上繳交結報
5/24 23:59 前於 moodle 接受補交，分數以 7 折計算