## Slide 1: 3D computer graphic
Basis for real-time rendering and GPU architecture
劉哲宇,Liou Jhe-Yu

## Slide 2: Motivation for learning graphics fundamentals
Q: I’m an architect. I do hardware, not algorithms. Can’t we just skip ahead to the case study?
A: Not really. You can’t understand 3D graphics architectures without understanding 3D graphics algorithms.
Q: Could I design my new Acme FlexiGPU architecture by optimizing for current graphics applications/ traces/benchmarks?
A: No, not if you want your architecture to be relevant when it’s done.
3D Graphics Architecture Tutoral(2004), W.Mark and H. Moreton, NVIDIA.

## Slide 3
3D Graphics Architecture Tutorial(2004), W. Mark and H. Moreton, NVIDIA.

## Slide 4: Outline
3D computer graphic
Real-time rendering – using OpenGL fixed function pipeline(1.5).
  Geometry Stage
  Rasterization stage
From fixed to Programmable
  OpenGL shading pipeline

## Slide 5: 3D computer graphic
Use 3D geometric data that are stored in the computer and then perform some specific calculations to render them on a 2D image.
OpenGL Super Bible 3rd edition

## Slide 6: 3D computer graphic Phases
3D modeling
Layout and animation
Rendering
World of Warcraft, Blizzard entertainment

## Slide 7: Polygon modeling
Vertex
  Basic unit with geometry data
Triangle
  3 vertices
  Basic polygon
Curve surface
  Triangles * N

## Slide 8: Layout and animation
Place 3D object or vertex group.
Give them the relationship between time domain and movement vector.
  May involve with physic simulation or motion capture on the human or animal movement.

## Slide 9: Rendering problem
Given
  3D world
  (objects and materials)
  Light locations
  A viewpoint
Compute
  2D image scene from the
  viewpoint

## Slide 10: Rendering
Non real-time rendering
  Cannot achieve 15 FPS (Frame per second) in modern GPU.
  The most global illumination algorithm
    Ray-tracing, radiosity, etc.
  EX: movie for realistic image.
Created by Gilles Tran
Toy Story 3, Pixar Disney

## Slide 11: Rendering
Real-time rendering
  Can display over 15 FPS.
  For those interactive applications.
  EX. Video game.
Simplified lighting model
and use texture image.
EX: OpenGL, DirectX
Crysis, Electronic Arts

## Slide 12: What is OpenGL
Specify a series of abstract API.
Define its own virtual graphic pipeline.
Use APIs to control this pipeline and draw 3D image
  Programmer doesn’t need to communicate directly with real hardware.
Cross-platform, cross-language, royalty-free,…
The OpenGL fixed-function pipeline (before OpenGL 2.0) is a really good entry point to know how the real-time rendering works.

## Slide 13: Conventional OpenGL pipeline (OpenGL 1.5)

## Slide 14: Processing sequence of OpenGL
Transformation and lighting
Texture mapping
Triangle traversal and interpolation

## Slide 15: Geometry Stage
Model-view Transformation
Lighting
Projection Transformation
Primitive assemble
Clipping

## Slide 16: Transformation
Model-view
  Transform an object from object coordinate into world coordinate.
  Include translate, scale, and rotate matrix operation.
y
x
z
y
x
z
Translate

## Slide 17: Transformation
Projection
  Mapping 3D point onto 2D plane
  Orthogonal vs. Perspective
Perspective projection
  Objects in the distance appear smaller than objects close by.

## Slide 18: Lighting
Created by Hugo Elias

## Slide 19: Lighting
Realistic render equation

## Slide 20: Lighting in OpenGL
OpenGL refines rendering equation
  Break optical phenomena into three lighting models.
  Break visible spectrum into red, green, and blue component.
Component
  Lighting source position
  Object position
  Observation position
  Object surface normal
  Color material of light and object
Lighting must be done in world coordinate
  After model-view but before projection

## Slide 21: Lighting in OpenGL
3 lighting models in OpenGL
Ambient
  Environment lighting
Diffuse
  Object receives light effect and reflect its own color.
Specular
  In particular angle, object will completely reflect light color.

## Slide 22: Lighting in OpenGL
OpenGL’s lighting equation
  approximated equation to solve rendering problem.
  No integrity and recursion.
Ambient
Diffuse
Specular

## Slide 23: Lighting in OpenGL
Ambient
Diffuse
Specular
Amb + Diff
Diff + Spec
All

## Slide 24: Surface shading model
Per-Vertex lighting
  Flat shading
    One polygon, one surface normal.
  Gouraud shading
    One polygon, three normals on three vertices.
Per-Pixel lighting
  Phong shading
    One polygon has lots of normal value for every pixel.

## Slide 25: Surface shading model
Flat shading
Gouraud shading
Phong shading

## Slide 26: Primitive Assembly and Clipping
Primitive = basic 3D polygon (triangle)
Primitive Assembly
  Gather three vertices into one triangle.
Clipping
  Clip the triangle which is partially outside the view volume into new triangle set.

## Slide 27: Rasterization Stage
Triangle Setup, traverse and interpolation
Anti-aliasing
Texture mapping & filter
Per-fragment operation

## Slide 28: Triangle traverse and interpolation
Purpose: decompose a triangle into pixels.
Triangle traverse
  Finding whether pixels are inside a triangle or not
Interpolation
  Give those pixels property from the original triangle.
  Color, texture coordinate, and so on.

## Slide 29: Anti-aliasing
Sample more sub-pixels then
combine them into one final pixel.

## Slide 30: Texture mapping
  Texture is not necessary if…
  Use lots, lots, lots, of tiny polygons to present a 3D object.
Why do we need texture?
  Give the object surface more details.
  Decrease polygon complexity, and increase performance.

## Slide 31: Texture mapping Downgrade polygon complexity and represent the detail
Path of exile, Grinding Gear Games

## Slide 32: Texture mapping
Basic texture mapping
  Give the fragment color
Procedure texture mapping
  Give the fragment physic property and adjust the color.
  Ex. Normal mapping

## Slide 33: Texture mapping normal mapping
Supported by OpenGL 1.5
An approach to per-pixel lighting.
Have a normal map which restores the original surface normal at each texel.
  (R,G,B) -> (x,y,z)
Re-do simplified lighting operation in texture mapping.

## Slide 34: Texture mapping normal mapping example

## Slide 35: Texture filter
Pixel <-> texel
  seldom one by one mapping.
The filter method decides whose texels will map to the specific pixel.

## Slide 36: Per-fragment operation
The pixel flying in the OpenGL pipeline is considered as a fragment.

## Slide 37: Painter algorithm
Visible problem.
Sorting polygons by depth and paint them in this sorting result.
Unable to solve cyclic overlap or piercing polygons

## Slide 38: Z-buffer algorithm (Depth Test)
Prosise , How Computer Graphics Work Prosise

## Slide 39: Alpha blending
Blend color from fragments and relative pixels in frame buffer.
  For transparent object
However, alpha blending has image defect with depth test in some case.

## Slide 40: Alpha blending’s race condition (Order-dependent transparent)
Use painter algorithm to fix it (depth sorting)
  Draw all opaque objects with depth test on.
  Get drawing order by sorting transparent objects.
  Draw transparent object in order with depth test on but depth write off.
Take care by programmer, not OpenGL……

## Slide 41: OpenGL Conclusion
Programmer:
  Prepare raw data.
  Place Object and lighting source.
  Optional operation.
    Sort object if alpha blending is needed.
OpenGL (Hardware)
  Calculating the effect between light and object.
  Transforming 3D object into 2D image.
  Executing texture operation

## Slide 42: Outline
3D computer graphic
Real-time rendering – using OpenGL fixed function pipeline(1.5).
  Geometry Stage
  Rasterization stage
From fixed to Programmable
  programmable shading pipeline

## Slide 43: Texture operation wants more flexibility
In OpenGL 1.5, normal mapping can be “partially” achieved by calling and setting parameter in glTexEnv API.
  API does know what is dot operation.
If I want to execute vecA Ω vecB in texture operation.
  OpenGL : Ω ????

## Slide 44: Lots of per-pixel lighting application under texture mapping
Color map, normal map, height map, light map, XXX map, ……, a lots of procedure map.
  And their combination.
EX: parallax occlusion mapping.
  Combine normal and height map
Normal mapping
Parallax occlusion mapping

## Slide 45: OpenGL 1.5 fixed function pipeline

## Slide 46: OpenGL 2.0 programmable pipeline

## Slide 47: DirectX 10 pipeline (OpenGL 4.0)
Input primitive
Vertex Shader
Geometry Shader
Rasterizer
Fragment Shader
Per-fragment operation
Video memory
(Texture,
Buffer,)

## Slide 48: Geometry shader and tessellation
Dynamic Generate/delete polygon.
Parallax occlusion mapping
Tessellation

## Slide 49: Programming pipeline with programmer
Advantage:
  Freedom
    More procedure texture applications, better image quality.
    Special post production effect.
    A solution for blending’s ordering problem can be made in advanced shader architecture without CPU pre-sorting.
    Step forward to ray-tracing.
Disadvantage
  No built-in light model and transformation function.

## Slide 50: Fixed pipeline’s game example (OpenGL 1.5)
Doom 3 (2003), id Software

## Slide 51: Programmable pipeline’s game ex.
Crysis 2 (2011), Crytek, Electronic Arts

## Slide 52: Trend of application
Maintain the final image quality but decrease polygon complexity.
Simplify per-vertex lighting algorithm.
Use multi layer texture to reconstruct per-pixel lighting and shadow effect.
  Make lighting equation closer to the rendering equation.

## Slide 53: Not everything is programmable
Primitive assembly, clipping, and culling.
Triangle traverse and interpolation.
Texture filter
Some per-fragment operation

## Slide 54
GPU Architecture?
See you next week
Thank you