## Slide 1: From ESL to Silicon
Jhe-Yu Liou

## Slide 2: Outline
From ESL to Silicon
From SIMD to SIMT
The challenge of SIMT
Conclusion

## Slide 3: From ESL to Silicon CPU
ARM v5 instruction compatible dual core.
Full-system verification capability
  Linux kernel 2.6 boot up.
Continue to focus on issue on power consumption, cache efficiency.

## Slide 4: From ESL to Silicon Network and Virtualization
A CASL hypervisor,
  so called a Virtual Machine Monitor (VMM).
A timing approximated TCP/IP offload engine.
Full system verification with
  Multiple guest OS.
  Communication with another computer by real Ethernet interface.

## Slide 5: From ESL to Silicon GPU
Support OpenGL ES 1.1
  Fixed function pipeline
Both pure C model and gate-level RTL model are presented.
Full system simulation environment with QEMU
  Debian, kernel 2.6.18

## Slide 6: From SIMD to SIMT
SIMD – single instruction multiple data.
Often referred as vector-based instruction.
  High level language:
    OpenGL Shading language.
    Template-based vector library in C++ (SSE-like instruction wrapper)
  Low level language:
    x86 SSE or AVX instruction set
    ARM NEON instruction set
    Nvidia NVGP4 pseudo assembly language.

## Slide 7: From SIMD to SIMT SIMD example
MUL.F R1.xyz, R1.z, R0
  R1.x = R1.z * R0.x
  R1.y = R1.z * R0.y
  R1.z = R1.z * R0.z
  R1.w = (nothing)
OpenGL Shading program (fragment) | NVGP4 pseudo assembly
vec3 c1, c2; vec3 eyeVector = vec3(0.0, 0.0, 1.0) c1 = texture2D( ColorMap, UV ).rgb; c2 = texture2D( NormalMap, UV ).rgb; c2 = c2*2 - vec3(1.0, 1.0, 1.0); color = c1 * dot(c2, eyeVector); | TEMP R0, R1; TEX.F R0.xyz, fragment.attrib[0], texture[0], 2D; TEX.F R1.z, fragment.attrib[0], texture[1], 2D; MUL.F R1.xyz, R1.z, R0; MAD.F result_color0.xyz, R1, {2}.x, -R0; END

## Slide 8: From SIMD to SIMT SIMD conclusion
The programmer itself has to take care the vector operation and optimization if possible.
  It’s not realistic to fully depend on compiler.
  May waste the execution power if only partial vector elements are required.

## Slide 9: From SIMD to SIMT SIMD conclusion (cont.)
Our OpenGL GPU simulator shows only about 30%~70% utilization in NVGP4 vector-based shader core.
Part of POM fragment shader in NVGP4 assembly
DP3.F R0.x, frag.attrib[1], frag.attrib[1]; RSQ.F R0.x, R0.x; MUL.F R1.xyz, R0.x, frag.attrib[1]; DIV.F R2.xy, R1, R1.z; RSQ.F R0.x, R0.y; MUL.F R2.zw, R2.xyxy, {-0.0057142857}.x; MUL.F R0.xyz, R0.x, frag.attrib[2]; MOV.F R2.xy, frag.attrib[0]; MOV.F R3.xy, {0}.x; MOV.F R3.z, {1}.x; MOV.F R1.w, {0}.x;

## Slide 10: From SIMD to SIMT
SIMT – single instruction multiple thread
  This terminology is introduced by Nvidia.
SIMT is a kind of execution model on hardware.
  Not an instruction set.
  Still within the concept of SIMD.
Working on narrow domain of programming model
  Like OpenGL and OpenCL

## Slide 11: From SIMD to SIMT SIMT execution model
Using OpenGL as example.
19200 vertices => 19200 threads
Each thread has its own data=>
position, normal vector, etc.
Shader program =>
for lighting calculation
Each thread will execute the same program here with different data from its own.

## Slide 12: From SIMD to SIMT SIMT execution model
Decode one instruction for multiple execution units.
  Ex: 16 exec units
The programmer cares about the programming model, instead of operations.
  Hardware controls the execution flow and thread dispatch.
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
Instruction
Decode
Shared register
Pool

## Slide 13: From SIMD to SIMT SIMD instruction + SIMT model?
SIMD/SIMT, they can co-exist with each other.
Instruction
Decode
Shared register
Pool
EU
EU
EU
EU
Vector exec unit
EU
EU
EU
EU
Vector exec unit

## Slide 14: From SIMD to SIMT scalar SIMT vs SIMD + SIMT
16 scalar cores vs 4 4-lane vector cores?
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
EU
decode
register
decode
register
EU
EU
EU
EU
Vector exec unit
EU
EU
EU
EU
Vector exec unit
EU
EU
EU
EU
Vector exec unit
EU
EU
EU
EU
Vector exec unit

## Slide 15: From SIMD to SIMT scalar SIMT vs SIMD + SIMT
Using scalar core in SIMT.
  Advantage
    Increase the execution unit’s utilization.
    Even a vector based instruction can be simply divided into scalar part.
  Disadvantage
    More threads executed at same time means more thread-related data kept in registers.
We have an on-going project worked with ITRI
  HSAIL-based SIMT shader processor

## Slide 16: The Challenge of SIMT
How SIMT executes a branch instruction?
  Which one is the target instruction if condition execution is involved?
Thread 1
R0 = 0
Thread 2
R0 = 0
Thread 3
R0 = 1
Thread 4
R0 = 1
If (R0 == 1)
R1 = 0;
else
R1 = 1;
If (R0 == 1)
R1 = 0;
else
R1 = 1;
If (R0 == 1)
R1 = 0;
else
R1 = 1;
If (R0 == 1)
R1 = 0;
else
R1 = 1;

## Slide 17: The Challenge of SIMT divergence
Divergence
  Threads are going in different direction and are not uniform anymore.
Naïve Solution – go through every code path.
If (R0 == 1) {
R1 = 0;
if (R7 == 1)
R2 = 1
}
else
R1 = 1;
Cycle 1
Cycle 2
Cycle 3

## Slide 18: The Challenge of SIMT divergence
This is why the traditional Ray-tracing is still relied on cluster server (processor)
  Photorealistic rendering method
  Can be highly parallel. (project million to billion ray around the scene)
  extreme high divergence in each ray-casting (thread) on photon collision, reflection, refraction, and diffusion computation.
Trace level: 5
Trace level: 50

## Slide 19: The Challenge of SIMT divergence
There is still some solution for divergence
  Hardware
    Using more instruction issue unit and aggressive scheduler.
    Trade-off between silicon area and computation power.
  Software
    Avoid branch operation. (depend on hardware and instruction architecture)
      a = clamp( (b - c)*99999.0, 0.0, 1.0)
      if (b-c) > 0
      a = 1.0;
      else
      a = 0.0;

## Slide 20: Conclusion
There are lots of issues about trade-off between utilization and computation power.
  Deeper data parallel or aggressive scheduler?
  Strongly application specific.

## Slide 21: If you are interesting in Graphic
Web: http://lioujheyu.synology.me/~git/ogles1_1/
Git: http://lioujheyu.synology.me/~git/index.cgi/ogles1_1.git/