## Slide 1: Lecture 2 Case study : 1D-PE Design for Convolution Layer work from T-C Wu
Chung-Ho Chen
NCKU EE

## Slide 2: Deep Learning Accelerators
Intensive Memory Access and Computation
S. Mitra/Standford
Abundant-Data Computing
https://beyondcmos.ornl.gov/documents/Panel_Session-Mitra.pdf
AI accelerator
development challenges
Intelligent data fetcher
Data reuse strategies in MAC (Multiply-Accumulate) PE arrays
Quantization scheme in MAC
Advanced in-memory computing analog PE
Design and simulation platform
Source: https://blocksandfiles.com/2019/02/11/ibms-ai-chips-change-phase/

## Slide 3: Putting into Perspective
Weight (Digital)
Weight (Digital)
Weight (Analog)
Weight (Analog)
Input (Digital)
Input (Analog)
Input (Analog)
Input (Digital)
Physical
Data
Physical
Data
ADC
DRAM/SRAM
Flash/RRAM
Interface
Digital, Analog MAC
Interface
Analog MAC
Analog MAC
Inter-
face
Analog MAC
Analog signal
Digital code

## Slide 4: AI Accelerator Design/Simulation Framework
Memory technologies
SRAM
Flash
Non-volatiles
DRAM
Deep Learning
System-Level Analysis
Architecture Exploration
Implementation
RTL, FPGA, Silicon
DL applications
Yolov3,
GAN…..
Input type (A or D), data reuse, execution time, energy

## Slide 5
LLVM intrinsic support for NNP instruction
Define intrinsic function for convolution, for instance, in LLVM, so that it can generate the assembly code for NNP.
to go with RISC-V or ARM
TVM Tuning
VTA as example -> Qbit DLA
DLA
Graph optimization
operator fusion, constant precompute, layout transform
Tensor Compute Description: tensor compute library,
tensor index expression (description language for
scheduling and optimization)
TVM: An Automated End-to-End Optimizing Compiler for Deep Learning
University of Washington- CSE

## Slide 6: DL Graph Compiler for AI ASIC
C Code Based Compiler
  Given the interface spec or API of DMA and DL NNP
  Read DL optimizer IR, or DL model config./weight, generate the sequence control C code
  Use C compiler of the target CPU
Assembly Code Based
  LLVM intrinsic functions for the target CPU
    Adding the instructions for DMA and NNP
  LLVM compiler for the target CPU

## Slide 7: Neural-Net Processor (NNP) Code Generation
Operators in AI graph are executed in either the RISC-v (or ARM) processor or the NNP
Define instructions for NNP operators.
Define operation granularity for NNP instructions
  Large (Convolution)
  Small (MAC), should be an enhanced version of RISC-V or ARM’s MAC

## Slide 8: Revisit Convolution Operation
N: # of channels for input map as well as kernel
M: # of filters or kernels, K: size of a filter, which keeps weights
The number of output channels is the number of filters used.
Partial sum of channel i, PSi: conv of channel i (the ith input map * the ith channel of a filter)
Total sum, where N is the number of channels
…
…
…
…
*
=
H
L
N
M
I
J
M: # of filters
K
K
Kernel Size = K*K*N*M
Output Size = I*J*M
Input Size = H*L*N
N channels
Total sum
N: # of channels

## Slide 9: A Convolution Unit; things to ponder
PE structure (fixed MACs or not)
  Determine how many MACs in a PE
Single PE array structure (parallelism)
Multiple PE arrays (scalable performance)
More importantly,
  how to reuse data
  how to operate on various size of kernels
  how to effectively use the PEs
Hardwired or software (CPU) controller
  So that runtime can call,
  or APIs that a code generator can use
  and hence produce the runtime library

## Slide 10: Data Reuse
1
Input Reuse
Output Reuse
Weight Reuse
Layer Reuse
Input
Weight
Partial Sum
Output
Ch1
Ch2
Ch3
Input
1
2
3
Weight
Partial Sum
Output
Input
Weight
Partial Sum
Output
Layer 1
Layer 2
Layer 3
Layer 4
DRAM
DRAM
Input Reuse (Input stationary)
  Load input data only once.
  Load all filters of the same channels at the same time.
  Need storing all partial sums for all filters.
Output Reuse (Output stationary)
  One filter (of its all channels) at a time.
Weight Reuse (Weight stationary)
  Weight are loaded only once, and stored in the Weight SRAM.
Layer Reuse
  The input and output of the two adjacent layers are the same.
  Only the first input and the last output need to transmission with the external memory.
  May need a huge internal memory space.
Ch1
Ch3
Ch2
3 channels, 3 filters of their channel 1
3 Partial sums from 3 filters
filter 1 of all its channels

## Slide 11: Tile Reuse: Operation from Tile View
Tile reuse: An input map is divided into Tiles.
Tile Reuse: A tile is brought in from DRAM and stays stationary.
To do this, M copies of weights of the same channel are made ready. Weights are stationary for the same input tile. (what if M < = # of PEs?)
How to allocate convolution task to PEs?

## Slide 12: Tile Reuse : Next tile
Order of tile processing: Same tile position of the next channel
Load new weights for the corresponding channel
For this channel, we can accumulate partial sum from the previous channel
M (number of filters) copies of the partial sum are produced
Partial sum of ch1 + ch2

## Slide 13: Tile view: Last tile of the last channel
At the end of last tile of the last channel: accumulate the total SUM for output
for that tile.
M output maps

## Slide 14
Partial sum
Partial sum
Partial sum
Partial sum
Partial sum
Partial sum
Output
Output
Output
Output map
Tile Reuse in Action

## Slide 15: Tile Reuse - Tile Overlap
Input Map
Input tile
1
Input tile
2
H
L
T
T
H : input map height
L : input map width
T : tile size
R : remainder tile height or width
K : kernel size
S : stride
overlap
T
T
R
T
T
R
Overhead for tile 2= 7.7 % (4/52) for T = 52, K= 3, S= 1
in term of pixels

## Slide 16: Convolution PE Unit
Per-filter based convolution task allocation to a PE
The same input is broadcast to all PEs for convolution operations
Parallel convolution operations on multiple filters for the same input data
Weight registers
Broadcast from SRAM bus

## Slide 17: Per-filter based conv. task allocation
Assume # of filters M=32, # of PEs =32
  If M >= 32, then batch
  If M < 32, 32-M PEs idle
Allocate one filter to a PE and compute channel by channel for tile-sized input
Synchronization of all PEs to the same input.
  Each PE receives the same 9 input pixels
Tile order: channel by channel tile order (why? easy to accumulate PS)
Load all 32 filters
filter 1
filter 2
PE1
PE2

## Slide 18: Partial sum accumulated PE design
Partial sum from the previous channel tile is added with the current channel convolution result.
  For a PE, it needs only one partial sum output memory which is reused until the total sum is accumulated.

## Slide 19: Tile view: Operation within a Tile (1/2)
Input tile i of input channel j
I0
I1
I2
I3
I4
I51
I52
I53
I54
I55
I56
I103
…
…
I104
I105
I106
I107
I108
I155
…
I156
I157
I158
I159
I160
I207
…
I208
I209
I210
I211
I212
I259
…
I2652
I2653
I2654
I2655
I2656
I2703
…
…
…
…
…
…
…
52
52
…
…
…
…
…
…
…
…
…
…
…
…
…
I0
I1
I2
I52
I53
I54
I104
I105
I106
I0
I1
I2
I52
I53
I54
I104
I105
I106
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 1
Kernel 1
I0
I1
I2
I52
I53
I54
I104
I105
I106
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 32
Kernel 32
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
tile i output in output SRAM for Kernel 1
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
tile i output in output SRAM for Kernel 32
…
Input SRAM Read
PEs
(multiply-and-accumulate)
Output SRAM Write
Sliding
Input broadcast

## Slide 20: Tile view: Operation within a Tile (2/2)
Input broadcast
Input tile i of channel j
I0
I1
I2
I3
I4
I51
I52
I53
I54
I55
I56
I103
…
…
I104
I105
I106
I107
I108
I155
…
I156
I157
I158
I159
I160
I207
…
I208
I209
I210
I211
I212
I259
…
I2652
I2653
I2654
I2655
I2656
I2703
…
…
…
…
…
…
…
52
52
…
…
…
…
…
…
…
…
…
…
…
…
…
I1
I2
I3
I53
I54
I55
I105
I106
I107
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 1
Kernel 1
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 32
Kernel 32
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Input SRAM Read
PEs
(multiply-and-accumulate)
Output SRAM Write
sliding
tile i output in output SRAM for Kernel 1
tile i output in output SRAM for Kernel 32

## Slide 21: Tile view: Operation within a Tile (2/2) Revision
Input broadcast
Input tile i of channel j
I0
I1
I2
I3
I4
I51
I52
I53
I54
I55
I56
I103
…
…
I104
I105
I106
I107
I108
I155
…
I156
I157
I158
I159
I160
I207
…
I208
I209
I210
I211
I212
I259
…
I2652
I2653
I2654
I2655
I2656
I2703
…
…
…
…
…
…
…
52
52
…
…
…
…
…
…
…
…
…
…
…
…
…
I1
I2
I3
I53
I54
I55
I105
I106
I107
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 1
Kernel 1
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 32
Kernel 32
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Input SRAM Read
PEs
(multiply-and-accumulate)
Output SRAM Write
sliding
tile i output in output SRAM for Kernel 1
tile i output in output SRAM for Kernel 32
This move has fetched
2/3 of the same pixels again.
This increases the on-chip SRAM accesses.
Remedy: See if the following possible.
Add 9 FFs btw input SRAM and PEs, and MUX the FFs output to the PE. Weights remain.
This time only fetches the required new pixels, I3, I55, I107.
MUX

## Slide 22: Optimization of Data Streaming From SRAM
A scheme to reduce 2/3 fetches of data from SRAM
New column data D2 are loaded into the FFs that release D0 for S=1
D1
FFs
D0
D2
D0
FFs
D2
D1
MUX
PED0
PED2
D0 D1 D2
Convolution block: Column data
Weights remain at their position
Allocated to process D0

## Slide 23: Global view: Per-filter Based Computation In a tile 1/5
3x3 kernel

## Slide 24: Global view: Per-filter Based Computation in the same tile 2/5
3x3 kernel

## Slide 25: Global view: Per-filter Based Computation in the same tile 3/5
3x3 kernel

## Slide 26: Global view: Per-filter Based Computation in the same tile 4/5
3x3 kernel

## Slide 27: Global view: Per-filter Based Computation change channel 5/5
3x3 kernel
Same input
Change channel kernels

## Slide 28: Project – part A: Intelligent Data Fetcher (1/3)
Problem statement: Propose a SRAM memory system and intelligent data fetcher design that can effectively prepare and align data to the PEs.
At the beginning we will provide you the DRAM model of Verilog and SystemC code. You need to put the input data and weights we provided into DRAM.
Different framework’s data formats will be placed in memory in different ways. The two most common data formats are NCHW and NHWC, so you need to choose one of the following data formats and your data should be placed like the form below.

## Slide 29: Project – part A: Intelligent Data Fetcher (2/3)
Propose a SRAM memory system. You can analyze which data reuse method is better and evaluate the SRAM size before designing, because this may affect your performance.(ex. Ping-pong Input SRAM, Weight SRAM)
Design an intelligent data fetcher(DMA) which can fetch data from DRAM then stores it into the SRAM in the proper order needed for the PE unit.
Since project part-B and part-C require you to design a PE accelerator, you need to think about a complete process to allow PE to receive data efficiently.

## Slide 30: Project – part A: Intelligent Data Fetcher (3/3)
Input image size : 416(height) * 416(width) * 3(channel)
Filter : 16 3(height) * 3(width) * 3(channel)
Padding = 0 , Stride = 1
Size of input SRAM and weight SRAM :
You can decide the SRAM size and how to design it, but you need to explain why you want to do this and write it into the report.
DMA :
You can use a start signal to tell DMA to start moving data. When all data is moved, you need an interrupt signal to inform the CPU that the task is complete.
Can be designed with RTL or SystemC code
Report due in 4 weeks.

## Slide 31: Kernel View: Oversize Kernel Handling (1/2)
Geometric directly mapping on 3x3 PEs
Example: 5x5 kernels (filters are colored)
Low PE utilization = 25/36 = 69.4%
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
A 3x3 PE core
5
5

## Slide 32: Kernel View: Row-major Order Kernel in Geometric Mapping, on different PEs (2/2)
5x5
7x7
11x11
32 PEs, each 9 MACs
Different color
means different kernels
10 kernels at a time
Run from channel 1 to N
for the given kernel. Then
go for another 10 kernels
if any
32 PEs
Spatial mapping

## Slide 33: Kernel View: Row-major Order Kernel Mapping on the Same PE for Oversize Kernel (1/2)
convolute a 5x5
kernel size
P
W
P: needed phases for oversize kernel
W: waste multiplier number for oversize kernel
k: kernel size
Kernel size | P | W
5 | 3 | 2
7 | 6 | 5
11 | 14 | 5
Same input broadcast to all PEs.
Suggesting that weights are loaded to PEs of the same row-major order.

## Slide 34: Kernel Row-major Order Mapping on the same 3x3 PE for Oversize Kernel (kernel + input view)
Get 9 tile data in row-major ordering of the kernel and send to all 32 PEs.
PE utilization = 25/27
5x5 kernel example: 1st batch
2nd batch
get the part of weights for 2nd batch
3rd batch

## Slide 35: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel in Action (1/6)
A filter on a PE
Input broadcast
to all PEs
Get the first 9 weights for each PE

## Slide 36: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel in Action (2/6)
Get the next 9 weights for each PE

## Slide 37
Kernel Row-major Order Mapping on the Same PE for Oversize Kernel in Action (3/6)
Get the last 7 weights for each PE

## Slide 38: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel (4/6)
Let’s move the
box for 1 pixel
Stride = 1
Get the first 9 weights for each PE again

## Slide 39: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel (5/6)
Get the next 9 weights for each PE again

## Slide 40: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel (6/6)
Get the last 7 weights for each PE again

## Slide 41: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel
Observations:
Reload 9 weights when switching to the next batch
Reload weights when striding
5x5:
B1
B2
B3
After first batch B1, need to load the next 9 weights for batch B2. This is a read
for weight SRAM.
5x5:
B1
B2
B3
Next convolution

## Slide 42: Optimization: Weight Stationary for Oversize Kernel
Optimization: Group the same batches in all different conv blocks in a tile together
Original
Optimized
B1
B2
B3
B1
B2
B3
B1
B2
B3
B1
B1
B1
B2
B2
B2
B3
B3
B3
=> 3 * 3 = 9 times
=> 3 times
Striding
Bi: batch order (or phase order) for a oversize kernel
A conv. block

## Slide 43: Optimization: Weight Stationary for Oversize Kernel
Optimization: Group the same batches in all different conv blocks in a tile together
Advantage:
  1: Address generation for input data becomes easy by using conv. block size as an offset.
  2: Avoid weight thrashing

## Slide 44: How about 1x1 kernels? The PE is 3x3.
YOLOv3-tiny | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers
 | Input map | Kernel size | Output map |  | 
conv1 | 416 x 416 x 3 | 3 | 416 x 416 x 16 | 50 % | 50 %
conv2 | 208 x 208 x 16 | 3 | 208 x 208 x 32 | 100 % | 100 %
conv3 | 104 x 104 x 32 | 3 | 104 x 104 x 64 | 100 % | 100 %
conv4 | 52 x 52 x 64 | 3 | 52 x 52 x 128 | 100 % | 100 %
conv5 | 26 x 26 x 128 | 3 | 26 x 26 x 256 | 100 % | 100 %
conv6 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 %
conv7 | 13 x 13 x 512 | 3 | 13 x 13 x 1024 | 100 % | 100 %
conv8 | 13 x 13 x 1024 | 1 | 13 x 13 x 256 | 100 % | 11.11 %
conv9 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 %
conv10 | 13 x 13 x 512 | 1 | 13 x 13 x 255 | 99.6 % | 11.07 %
conv11 | 13 x 13 x 256 | 1 | 13 x 13 x 128 | 100 % | 11.11 %
conv12 | 26 x 26 x 384 | 3 | 26 x 26 x 256 | 100 % | 100 %
conv13 | 26 x 26 x 256 | 1 | 26 x 26 x 255 | 99.6 % | 11.07 %
99.09 % | 68.8 %

## Slide 45: Optimization for 1x1 Kernel Size
When input map size is smaller than 52x52 (input tile size) and kernel size is 1x1, transfer more then 1 input map of different input channels to Input SRAM. The convolution of these input maps in the input SRAM would be executed at the same time. Assume Input SRAM size = tile size.
YOLOv3-tiny | Input map | Kernel size | Max input map # that Input SRAM can store | Input map # stored in Input SRAM
conv8 | 13x13 | 1 | 16 | 9
conv10 | 13x13 | 1 | 16 | 9
conv11 | 13x13 | 1 | 16 | 9
conv13 | 26x26 | 1 | 4 | 4
Example

## Slide 46: Optimization for 1x1 Kernel Size (1/4)
Get at max 9 channels of
kernel 1
Input maps
in DRAM
IR input maps
in Input SRAM
*
+
previous
psum
=
PE 1
Kernel 1
*
+
previous
psum
=
PE 2
Kernel 2
*
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
(max=9)
Partial sum
in Output SRAM
H x L is the dimension
of input map, e.g., 13x13
Less than tile size

## Slide 47: Optimization for 1x1 Kernel Size (2/4)
Input maps
in DRAM
IR input maps
in Input SRAM
*
+
previous
psum
=
PE 1
Kernel 1
*
+
previous
psum
=
PE 2
Kernel 2
*
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
(max=9)
Partial sum
in Output SRAM
Move for Stride = 1
Weight stationary

## Slide 48: Optimization for 1x1 Kernel Size (3/4)
Input maps
in DRAM
IR input maps
in Input SRAM
*
+
previous
psum
=
PE 1
Kernel 1
*
+
previous
psum
=
PE 2
Kernel 2
*
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
(max=9)
Partial sum
in Output SRAM
End of H x L convolutions

## Slide 49: Optimization for 1x1 Kernel Size (4/4)
Input maps
in DRAM
IR input maps
in Input SRAM
The rest of channels
Load channel weights
0
0
0
0
0
*
0
0
0
0
0
+
previous
psum
=
PE 1
Kernel 1
*
0
0
0
0
0
+
previous
psum
=
PE 2
Kernel 2
*
0
0
0
0
0
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
0
0
0
0
0
0
0
0
0
0
Partial sum
in Output SRAM

## Slide 50: Project – part B: PE accelerator
Continuing what you did last time with project-partA. You need to add PE unit to your design, then you need an output SRAM to store the partial sum or the result of the operation, and finally write it back to the DRAM.
You need to consider the following issues:
1. how to dispatch different kernel size to pe for calculation(3x3, 5x5)
2. PE array structure
3. PE utilization
4. data reuse
5. data streaming from SRAM to PE
RTL or SystemC code design
Report due in 4 weeks.

## Slide 51: Input SRAM Example
Pros
  Can get all data in a cycle
Cons
  Power consumption, datapath,
  Mux tree delay
Notes: Register File 2.704KB左右

## Slide 52: PEs’ utilization rate of YOLOv3-tiny
YOLOv3-tiny | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers | 2D PE- Utilization rate of 32x32 PEs
 | Input map | Kernel size | Output map |  |  | 
conv1 | 416 x 416 x 3 | 3 | 416 x 416 x 16 | 50 % | 50 % | 49.992 %
conv2 | 208 x 208 x 16 | 3 | 208 x 208 x 32 | 100 % | 100 % | 99.968 %
conv3 | 104 x 104 x 32 | 3 | 104 x 104 x 64 | 100 % | 100 % | 99.935 %
conv4 | 52 x 52 x 64 | 3 | 52 x 52 x 128 | 100 % | 100 % | 99.871 %
conv5 | 26 x 26 x 128 | 3 | 26 x 26 x 256 | 100 % | 100 % | 99.742 %
conv6 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 % | 99.485 %
conv7 | 13 x 13 x 512 | 3 | 13 x 13 x 1024 | 100 % | 100 % | 99.742 %
conv8 | 13 x 13 x 1024 | 1 | 13 x 13 x 256 | 100 % | 11.11 % → 99.81 % | 98.848 %
conv9 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 % | 99.485 %
conv10 | 13 x 13 x 512 | 1 | 13 x 13 x 255 | 99.6 % | 11.07 % → 99.41 % | 97.722 %
conv11 | 13 x 13 x 256 | 1 | 13 x 13 x 128 | 100 % | 11.11 % → 98.08 % | 95.545 %
conv12 | 26 x 26 x 384 | 3 | 26 x 26 x 256 | 100 % | 100 % | 99.914 %
conv13 | 26 x 26 x 256 | 1 | 26 x 26 x 255 | 99.6 % | 11.07 % → 44.27 % | 98.848 %
99.09 % | 91.66 % | 95.952 %

## Slide 53: PEs’ utilization rate of VGG16
VGG16 | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers | 2D PE- Utilization rate of 32x32 PEs | Eyeriss Num. of active PEs
 | Input map | Kernel size | Output map |  |  |  | 
conv1 | 224 x 224 x 3 | 3 | 224 x 224 x 64 | 100 % | 100 % | 86.182 % | 156 (93%)
conv2 | 224 x 224 x 64 | 3 | 224 x 224 x 64 | 100 % | 100 % | 99.995 % | 156 (93%)
conv3 | 112 x 112 x 64 | 3 | 112 x 112 x 128 | 100 % | 100 % | 99.992 % | 156 (93%)
conv4 | 112 x 112 x 128 | 3 | 112 x 112 x 128 | 100 % | 100 % | 99.996 % | 156 (93%)
conv5 | 56 x 56 x 128 | 3 | 56 x 56 x 256 | 100 % | 100 % | 99.990 % | 156 (93%)
conv6 | 56 x 56 x 256 | 3 | 56 x 56 x 256 | 100 % | 100 % | 99.995 % | 156 (93%)
conv7 | 56 x 56 x 256 | 3 | 56 x 56 x 256 | 100 % | 100 % | 99.995 % | 156 (93%)
conv8 | 28 x 28 x 256 | 3 | 28 x 28 x 512 | 100 % | 100 % | 99.990 % | 168 (100%)
conv9 | 28 x 28 x 512 | 3 | 28 x 28 x 512 | 100 % | 100 % | 99.995 % | 168 (100%)
conv10 | 28 x 28 x 512 | 3 | 28 x 28 x 512 | 100 % | 100 % | 99.995 % | 168 (100%)
conv11 | 14 x 14 x 512 | 3 | 14 x 14 x 512 | 100 % | 100 % | 99.982 % | 168 (100%)
conv12 | 14 x 14 x 512 | 3 | 14 x 14 x 512 | 100 % | 100 % | 99.982 % | 168 (100%)
conv13 | 14 x 14 x 512 | 3 | 14 x 14 x 512 | 100 % | 100 % | 99.982 % | 168 (100%)
100 % | 100 % | 98.928 % | 96.23 %

## Slide 54: PEs’ utilization rate of AlexNet
AlexNet | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers | 2D PE- Utilization rate of 32x32 PEs | Eyeriss Num. of active PEs
 | Input map | Kernel size | Output map |  |  |  | 
conv1 | 227 x 227 x 3 | 11 | 55 x 55 x 96 | 100 % | 96.03 % | 70.542 % | 154 (92%)
conv2 | 31 x 31 x 48 | 5 | 27 x 27 x 256 | 100 % | 92.6 % | 99.957 % | 135 (80%)
conv3 | 15 x 15 x 256 | 3 | 13 x 13 x 384 | 100 % | 100 % | 99.943 % | 156 (93%)
conv4 | 15 x 15 x 192 | 3 | 13 x 13 x 384 | 100 % | 100 % | 99.924 % | 156 (93%)
conv5 | 15 x 15 x 192 | 3 | 13 x 13 x 256 | 100 % | 100 % | 99.886 % | 156 (93%)
100 % | 97.726 % | 94.050 % | 90.2 %

## Slide 55: Convolution, Bias Addition, and ReLU PE Core
Convolution, bias ,and ReLU in PE

## Slide 56: Memory System
Data fetcher
DRAM
Memory
bus
Accelerator
SRAM
DMA controller
Intelligent fetcher
Arbiter

## Slide 57: Project – part C: Complete 1D PE accelerator
Continue project partA and partB, this time you need to finish a complete PE accelerator.
Your accelerator needs to be able to apply to different input map size and kernel size, and able to do the following things:
1. convolution
2. bias
3. Relu
In order to make your design more complete, you need to add bus and arbiter to your design.
Enhance your design by considering all the optimizations addressed so far.
Can be designed with RTL or SystemC code
Presentation due in final week.

## Slide 58: Thanks You
Machine Learning
Hello!! R2-D2