## Slide 1: Lecture 2 Domain Specific Computing Case study: 1D-PE Design for Convolution Layer part of the work from T-C Wu
Chung-Ho Chen
NCKU EE

## Slide 2: Deep Learning Accelerators
Intensive Memory Access and Computation
S. Mitra/Standford
Abundant-Data Computing
https://beyondcmos.ornl.gov/documents/Panel_Session-Mitra.pdf
AI accelerator
development challenges
Intelligent data fetcher
Data placement for PEs
Data reuse strategies in MAC (Multiply-Accumulate) PE arrays
Quantization scheme in MAC
Design and simulation platform (tools and software)
Advanced in-memory computing
Source: https://blocksandfiles.com/2019/02/11/ibms-ai-chips-change-phase/

## Slide 3: Putting into Perspective
Weight (Digital)
Weight (Digital)
Weight (Analog)
Weight (Analog)
Input (Digital)
Input (Analog)
Input (Analog)
Input (Digital)
Physical
Data
Physical
Data
ADC
DRAM/SRAM
Flash/RRAM
Interface
Digital, Analog MAC
Interface
Analog MAC
Analog MAC
Inter-
face
Analog MAC
Analog signal
Digital code

## Slide 4: AI Accelerator Design/Simulation Framework
Memory technologies
SRAM
Flash
Non-volatiles
DRAM
Deep Learning
System-Level Analysis
Architecture Exploration
Implementation
RTL, FPGA, Silicon
DL applications
Yolov3,
GAN…..
Input type (A or D), data reuse, execution time, energy

## Slide 5: Compute in Memory (CIM)
Why CIM?
  Data movement causes time and energy consumption
  Memory wall
  CiM advantages: 1) improve speed and area efficiency, due to computation directly in memory, and 2) very good energy efficiency, thanks to the analog MAC operations.
(a) Data movement from SRAM buffer to the processing elements in the conventional von Neumann architecture makes it the primary performance bottleneck in the execution of data-intensive workloads.
(b) The memory macros in a CiM structure are not limited to normal read and write operations. They can operate as a computing engine to perform MAC operations and minimize the amount of data that needs to be moved between the processor and the SRAMs.
Cons: PVT variation impact on analog computing. (Process, Voltage, Temperature)
  PVT-aware quantization training
IEEE Micro 2019 Zhixiao Zhang; Xin Si; Srivatsa Srinivasa; Akshay Krishna Ramanathan; Meng-Fan Chang
Recent Advances in Compute-in-Memory Support for SRAM Using Monolithic 3-D Integration

## Slide 6: TVM (Tensor Virtual Machine): An Automated End-to-End Optimizing Compiler for Deep Learning
A tensor is a generalization of vectors and matrices and is easily understood as a multidimensional array. It is a term and set of techniques known in machine learning in the training and operation of deep learning models can be described in terms of tensors.
University of Washington- CSE
  Tianqi Chen and Thierry Moreau, University of Washington; Ziheng Jiang, University of Washington, AWS; Lianmin Zheng, Shanghai Jiao Tong University; Eddie Yan, Haichen Shen, and Meghan Cowan, University of Washington; Leyuan Wang, UC Davis, AWS; Yuwei Hu, Cornell; Luis Ceze, Carlos Guestrin, and Arvind Krishnamurthy, University of Washington
TVM
Frameworks
Deployable Module
Facebook ML
Compiler:
Glow
Google
TensorFlow

## Slide 7
Graph level optimization: operator fusion (conv+Relu. e.g.),
constant folding, quantization (ft32 to int8 or ft16)
Tensor Compute Description (algorithm)
tensor compute library,
tensor index expression.
TVM
CodeGen: Produce platform-specific code
Runtime
Hardware
Tensor level (MAC, e.g.) optimization, scheduling
according to your hardware (SIMD, vector, e.g.)
Relay IR (Parsing different frameworks into Relay IR))

## Slide 8: Revisit Convolution Operation
N: # of channels for input map as well as kernel
M: # of filters or kernels, K: size of a filter, which keeps weights
The number of output channels is the number of filters used.
Partial sum of channel i, PSi: conv of channel i (the ith input map * the ith channel of a filter)
Total sum, where N is the number of channels
…
…
…
…
*
=
H
W
N
M
I
J
M: # of filters
K
K
Kernel Size = K*K*N*M
Output Size = I*J*M
Input Size = H*W*N
N channels
Total sum: sum of element-wise multiplications
N: # of channels

## Slide 9: Deep Convolution NNs
How deep is deep?
Up to 1000 layers of CNNs
Fig. from Yu-Hsin Chen, Eyeriss

## Slide 10: A Convolution Unit; things to ponder
PE structure (fixed MACs or not)
  Determine how many MACs in a PE
Single PE array structure (parallelism)
Multiple PE arrays (scalable performance)
More importantly,
  how to reuse data
  how to operate on various size of kernels
  how to effectively use the PEs
Hardwired or software (CPU) controller
  So that runtime can call,
  or APIs that a code generator can use
  and hence produce the runtime library

## Slide 11: Energy Cost
Memory hierarch makes sense
  65 nm process
Fig. from Yu-Hsin Chen, Eyeriss

## Slide 12: Weight Stationary
Filters of different dimension keep weights
Minimize weight read energy consumption
Weights are with the PEs.
Ex: Different pixel enters different MAC and accumulates PS for a convolution block here.
  Then go for a different CB of the same channel, but weights stay. If you switch channel, then weights change.
Weight stationary example
  Google TPU
Fig. from Yu-Hsin Chen, Eyeriss

## Slide 13: Output Stationary
What is partial sum?
  A multiplication output
  Accumulated output of a convolutional block for multiple channel format
minimize partial sum read/write energy consumption.
Partial sum is accumulated with the PEs.
  Systolic array
Fig. from Yu-Hsin Chen, Eyeriss

## Slide 14: Tile Reuse: Operation from Tile View
Tile reuse: An input map is divided into Tiles.
Tile Reuse: A tile is brought in from DRAM and stays stationary.
To do this, M copies of weights of the same channel are made ready. Weights are stationary for the same input tile. (what if M < = # of PEs?)
How to allocate convolution task to PEs?

## Slide 15: Tile Reuse : Next tile
Order of tile processing: Same tile position of the next channel
Load new weights for the corresponding channel
For this channel, we can accumulate partial sum from the previous channel
M (number of filters) copies of the partial sum are produced
Partial sum of ch1 + ch2

## Slide 16: Tile view: Last tile of the last channel
At the end of last tile of the last channel: accumulate the total SUM for output
for that tile.
M output maps

## Slide 17
Partial sum
Partial sum
Partial sum
Partial sum
Partial sum
Partial sum
Output
Output
Output
Output map
Tile Reuse in Action

## Slide 18: Tile Reuse - Tile Overlap
Input Map
Input tile
1
Input tile
2
H
L
T
T
H : input map height
L : input map width
T : tile size
R : remainder tile height or width
K : kernel size
S : stride
overlap
T
T
R
T
T
R
Overhead for tile 2= 7.7 % (4/52) for T = 52, K= 3, S= 1
in term of pixels

## Slide 19: Convolution PE Unit
Per-filter based convolution task allocation to a PE (9 MACs)
The same input is broadcast to all PEs for convolution operations
Parallel convolution operations on multiple filters for the same input data
Weight registers
Broadcast from SRAM bus

## Slide 20: Per-filter based conv. task allocation
Assume # of filters M=32, # of PEs =32
  If M >= 32, then batch
  If M < 32, 32-M PEs idle
Allocate one filter to a PE and compute channel by channel for tile-sized input
Synchronization of all PEs to the same input
  Each PE receives the same 9 input pixels
Tile order: channel by channel tile order (why? easy to accumulate PS)
Load all 32 filters
filter 1
filter 2
PE1
PE2

## Slide 21: Partial sum accumulated PE design
Partial sum from the previous channel tile is added with the current channel convolution result.
  For a PE, it needs only one partial sum output memory which is reused until the total sum is accumulated.
  To reduce output SRAM access, we can add an RF to accumulated PSs in a tile, what is the size of this RF?

## Slide 22: Optimization for partial sum accumulation in RF
Add a RF of size of
  p = 1, s = 1, f = 1, for a tile n = 64
  Need to buffer : 64 + 2 -1 +1 x () = 66 x 66 per PE, too expensive?
Can we tradeoff for a smaller size?
  Smaller n,
  Or processing order, C wise first. Need an operation mapping strategy.
Output dimension
(+ 1 ) * (+ 1 )
+ 1 = 3
64
64

## Slide 23: Tile view: Operation within a Tile (1/2)
Input tile i of input channel j
I0
I1
I2
I3
I4
I51
I52
I53
I54
I55
I56
I103
…
…
I104
I105
I106
I107
I108
I155
…
I156
I157
I158
I159
I160
I207
…
I208
I209
I210
I211
I212
I259
…
I2652
I2653
I2654
I2655
I2656
I2703
…
…
…
…
…
…
…
52
52
…
…
…
…
…
…
…
…
…
…
…
…
…
I0
I1
I2
I52
I53
I54
I104
I105
I106
I0
I1
I2
I52
I53
I54
I104
I105
I106
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 1
Kernel 1
I0
I1
I2
I52
I53
I54
I104
I105
I106
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 32
Kernel 32
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
tile i output in output SRAM for Kernel 1
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
tile i output in output SRAM for Kernel 32
…
Input SRAM Read
PEs
(multiply-and-accumulate)
Output SRAM Write
Sliding
Input broadcast

## Slide 24: Tile view: Operation within a Tile (2/2)
Input broadcast
Input tile i of channel j
I0
I1
I2
I3
I4
I51
I52
I53
I54
I55
I56
I103
…
…
I104
I105
I106
I107
I108
I155
…
I156
I157
I158
I159
I160
I207
…
I208
I209
I210
I211
I212
I259
…
I2652
I2653
I2654
I2655
I2656
I2703
…
…
…
…
…
…
…
52
52
…
…
…
…
…
…
…
…
…
…
…
…
…
I1
I2
I3
I53
I54
I55
I105
I106
I107
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 1
Kernel 1
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 32
Kernel 32
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Input SRAM Read
PEs
(multiply-and-accumulate)
Output SRAM Write
sliding
tile i output in output SRAM for Kernel 1
tile i output in output SRAM for Kernel 32

## Slide 25: Tile view: Operation within a Tile (2/2) Revision
Input broadcast
Input tile i of channel j
I0
I1
I2
I3
I4
I51
I52
I53
I54
I55
I56
I103
…
…
I104
I105
I106
I107
I108
I155
…
I156
I157
I158
I159
I160
I207
…
I208
I209
I210
I211
I212
I259
…
I2652
I2653
I2654
I2655
I2656
I2703
…
…
…
…
…
…
…
52
52
…
…
…
…
…
…
…
…
…
…
…
…
…
I1
I2
I3
I53
I54
I55
I105
I106
I107
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 1
Kernel 1
I1
I2
I3
I53
I54
I55
I105
I106
I107
W0
W1
W2
W3
W4
W5
W6
W7
W8
x
x
x
x
x
x
x
x
x
+
psum
Updated psum
PE 32
Kernel 32
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
P0
P1
P2
P3
P4
P50
P51
P52
P53
P54
…
…
P100
P101
P102
P103
P104
…
P150
P151
P152
P153
P154
…
P200
P201
P202
P203
P204
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
…
Input SRAM Read
PEs
(multiply-and-accumulate)
Output SRAM Write
sliding
tile i output in output SRAM for Kernel 1
tile i output in output SRAM for Kernel 32
This move has fetched
2/3 of the same pixels again.
This increases the on-chip SRAM accesses.
Remedy: See if the following possible.
Add 9 FFs btw input SRAM and PEs, and MUX the FFs output to the PE. Weights remain.
This time only fetches the required new pixels, I3, I55, I107.
MUX

## Slide 26: Optimization of Data Streaming From SRAM
Problem: To reduce 2/3 fetches of data from SRAM
New column data D2 are loaded into the FFs that release D0 for S=1
D1
FFs
D0
D2
D0
FFs
D2
D1
MUX
PED0
PED2
D0 D1 D2
Convolution block: D/D1/D2 column
Weights remain at their position
Allocated to process
Column D0
Line Buffer
Filter 3x3
Feeding
D0/D1/D2 to PEs

## Slide 27: Global view: Per-filter Based Computation In a tile 1/5
3x3 kernel

## Slide 28: Global view: Per-filter Based Computation in the same tile 2/5
3x3 kernel

## Slide 29: Global view: Per-filter Based Computation in the same tile 3/5
3x3 kernel

## Slide 30: Global view: Per-filter Based Computation in the same tile 4/5
3x3 kernel

## Slide 31: Global view: Per-filter Based Computation change channel 5/5
3x3 kernel
Same input
Change channel kernels

## Slide 32: How about oversize or small size kernel ? >3x3, <3x3
Filters that have size large than 3x3 or less than 3x3?

## Slide 33: Kernel View: Oversize Kernel Handling (1/2)
Geometric directly mapping on 3x3 PEs
Example: 5x5 kernels (filters are colored)
Low PE utilization = 25/36 = 69.4%
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
A 3x3 PE core
5
5
8 x 4 (32) PE array

## Slide 34: Kernel View: Row-major Order Kernel in Geometric Mapping, on different PEs (2/2)
5x5
7x7
11x11
32 PEs, each 9 MACs
Different color
means different kernels
10 kernels at a time
Run from channel 1 to N
for the given kernel. Then
go for another 10 kernels
if any
32 PEs
Spatial mapping

## Slide 35: Kernel View: Row-major Order Kernel Mapping on the Same PE for Oversize Kernel (1/2)
convolute a 5x5
kernel size
P
W
P: needed phases for oversize kernel
W: waste multiplier number for oversize kernel
k: kernel size
Kernel size | P | W
5 | 3 | 2
7 | 6 | 5
11 | 14 | 5
Same input broadcast to all PEs.
Suggesting that weights are loaded to PEs of the same row-major order.

## Slide 36: Kernel Row-major Order Mapping on the same 3x3 PE for Oversize Kernel (kernel + input view)
Get 9 tile pixel in row-major ordering of the kernel and send to all 32 PEs.
PE utilization = 25/27
5x5 kernel example: 1st batch
2nd batch
get the part of weights for 2nd batch
3rd batch

## Slide 37: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel in Action (1/6)
A filter on a PE
Input broadcast
to all PEs
Get the first 9 weights for each PE

## Slide 38: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel in Action (2/6)
Get the next 9 weights for each PE

## Slide 39
Kernel Row-major Order Mapping on the Same PE for Oversize Kernel in Action (3/6)
Get the last 7 weights for each PE

## Slide 40: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel (4/6)
Let’s move the
box for 1 pixel
Stride = 1
Get the first 9 weights for each PE again

## Slide 41: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel (5/6)
Get the next 9 weights for each PE again

## Slide 42: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel (6/6)
Get the last 7 weights for each PE again

## Slide 43: Kernel Row-major Order Mapping on the Same PE for Oversize Kernel
Observations:
Reload 9 weights when switching to the next batch
Reload weights when striding
5x5:
B1
B2
B3
After first batch B1, need to load the next 9 weights for batch B2. This is a read
for weight SRAM.
5x5:
B1
B2
B3
Next convolution

## Slide 44: Optimization: Weight Stationary for Oversize Kernel
Optimization: Group the same batches in all different conv blocks in a tile together
Original
Optimized
B1
B2
B3
B1
B2
B3
B1
B2
B3
B1
B1
B1
B2
B2
B2
B3
B3
B3
=> 3 * 3 = 9 times
=> 3 times
Striding
Bi: batch order (or phase order) for an oversize kernel
A conv. block

## Slide 45: Optimization: Weight Stationary for Oversize Kernel
Optimization: Group the same batches in all different conv blocks in a tile together
Advantage:
  1: Address generation for input data becomes easy by using conv. block size as an offset.
  2: Avoid weight thrashing

## Slide 46: Data Streaming to PEs
Things to ponder
Previous switching FF scheme good for 3x3 kernel with 3x3 PE
How to make it work for kernel size other than 3x3?
  Configurable PE size that tailors to kernel size? Impact?

## Slide 47: How about 1x1 kernels? The PE is 3x3.
YOLOv3-tiny | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers
 | Input map | Kernel size | Output map |  | 
conv1 | 416 x 416 x 3 | 3 | 416 x 416 x 16 | 50 % | 50 %
conv2 | 208 x 208 x 16 | 3 | 208 x 208 x 32 | 100 % | 100 %
conv3 | 104 x 104 x 32 | 3 | 104 x 104 x 64 | 100 % | 100 %
conv4 | 52 x 52 x 64 | 3 | 52 x 52 x 128 | 100 % | 100 %
conv5 | 26 x 26 x 128 | 3 | 26 x 26 x 256 | 100 % | 100 %
conv6 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 %
conv7 | 13 x 13 x 512 | 3 | 13 x 13 x 1024 | 100 % | 100 %
conv8 | 13 x 13 x 1024 | 1 | 13 x 13 x 256 | 100 % | 11.11 %
conv9 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 %
conv10 | 13 x 13 x 512 | 1 | 13 x 13 x 255 | 99.6 % | 11.07 %
conv11 | 13 x 13 x 256 | 1 | 13 x 13 x 128 | 100 % | 11.11 %
conv12 | 26 x 26 x 384 | 3 | 26 x 26 x 256 | 100 % | 100 %
conv13 | 26 x 26 x 256 | 1 | 26 x 26 x 255 | 99.6 % | 11.07 %
99.09 % | 68.8 %

## Slide 48: Optimization for 1x1 Kernel Size
When input map size is smaller than 52x52 (input tile size) and kernel size is 1x1, transfer more then 1 input map of different input channels to Input SRAM. The convolution of these input maps in the input SRAM would be executed at the same time. Assume Input SRAM size = tile size.
YOLOv3-tiny | Input map | Kernel size | Max input map # that Input SRAM can store | Input map # stored in Input SRAM
conv8 | 13x13 | 1 | 16 | 9
conv10 | 13x13 | 1 | 16 | 9
conv11 | 13x13 | 1 | 16 | 9
conv13 | 26x26 | 1 | 4 | 4
Example
52x52 /(13x13) = 16 ( of different channels)
Limited by:
each PE has
9 MACs.

## Slide 49: Optimization for 1x1 Kernel Size (1/4)
Get at max 9 channels of
kernel 1
Input maps
in DRAM
IR input maps
in Input SRAM
*
+
previous
psum
=
PE 1
Kernel 1
*
+
previous
psum
=
PE 2
Kernel 2
*
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
(max=9)
Partial sum
in Output SRAM
H x L is the dimension
of input map, e.g., 13x13
Less than tile size

## Slide 50: Optimization for 1x1 Kernel Size (2/4)
Input maps
in DRAM
IR input maps
in Input SRAM
*
+
previous
psum
=
PE 1
Kernel 1
*
+
previous
psum
=
PE 2
Kernel 2
*
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
(max=9)
Partial sum
in Output SRAM
Move for Stride = 1
Weight stationary

## Slide 51: Optimization for 1x1 Kernel Size (3/4)
Input maps
in DRAM
IR input maps
in Input SRAM
*
+
previous
psum
=
PE 1
Kernel 1
*
+
previous
psum
=
PE 2
Kernel 2
*
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
(max=9)
Partial sum
in Output SRAM
End of H x L convolutions

## Slide 52: Optimization for 1x1 Kernel Size (4/4)
Input maps
in DRAM
IR input maps
in Input SRAM
The rest of channels
Load channel weights
0
0
0
0
0
*
0
0
0
0
0
+
previous
psum
=
PE 1
Kernel 1
*
0
0
0
0
0
+
previous
psum
=
PE 2
Kernel 2
*
0
0
0
0
0
+
previous
psum
=
PE 32
Kernel 32
…
H
L
N
input pixels
input pixels
input pixels
H
L
IR
0
0
0
0
0
0
0
0
0
0
Partial sum
in Output SRAM

## Slide 53: Input SRAM Example: Line Buffer Design
Pros
  Can get all data in a cycle
Cons
  Power consumption, datapath,
  Mux tree delay
Notes: Register File 2.704KB左右

## Slide 54: PEs’ utilization rate of YOLOv3-tiny
YOLOv3-tiny | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers | 2D PE- Utilization rate of 32x32 PEs
 | Input map | Kernel size | Output map |  |  | 
conv1 | 416 x 416 x 3 | 3 | 416 x 416 x 16 | 50 % | 50 % | 49.992 %
conv2 | 208 x 208 x 16 | 3 | 208 x 208 x 32 | 100 % | 100 % | 99.968 %
conv3 | 104 x 104 x 32 | 3 | 104 x 104 x 64 | 100 % | 100 % | 99.935 %
conv4 | 52 x 52 x 64 | 3 | 52 x 52 x 128 | 100 % | 100 % | 99.871 %
conv5 | 26 x 26 x 128 | 3 | 26 x 26 x 256 | 100 % | 100 % | 99.742 %
conv6 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 % | 99.485 %
conv7 | 13 x 13 x 512 | 3 | 13 x 13 x 1024 | 100 % | 100 % | 99.742 %
conv8 | 13 x 13 x 1024 | 1 | 13 x 13 x 256 | 100 % | 11.11 % → 99.81 % | 98.848 %
conv9 | 13 x 13 x 256 | 3 | 13 x 13 x 512 | 100 % | 100 % | 99.485 %
conv10 | 13 x 13 x 512 | 1 | 13 x 13 x 255 | 99.6 % | 11.07 % → 99.41 % | 97.722 %
conv11 | 13 x 13 x 256 | 1 | 13 x 13 x 128 | 100 % | 11.11 % → 98.08 % | 95.545 %
conv12 | 26 x 26 x 384 | 3 | 26 x 26 x 256 | 100 % | 100 % | 99.914 %
conv13 | 26 x 26 x 256 | 1 | 26 x 26 x 255 | 99.6 % | 11.07 % → 44.27 % | 98.848 %
99.09 % | 91.66 % | 95.952 %

## Slide 55: PEs’ utilization rate of VGG16
VGG16 | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers | 2D PE- Utilization rate of 32x32 PEs | Eyeriss Num. of active PEs
 | Input map | Kernel size | Output map |  |  |  | 
conv1 | 224 x 224 x 3 | 3 | 224 x 224 x 64 | 100 % | 100 % | 86.182 % | 156 (93%)
conv2 | 224 x 224 x 64 | 3 | 224 x 224 x 64 | 100 % | 100 % | 99.995 % | 156 (93%)
conv3 | 112 x 112 x 64 | 3 | 112 x 112 x 128 | 100 % | 100 % | 99.992 % | 156 (93%)
conv4 | 112 x 112 x 128 | 3 | 112 x 112 x 128 | 100 % | 100 % | 99.996 % | 156 (93%)
conv5 | 56 x 56 x 128 | 3 | 56 x 56 x 256 | 100 % | 100 % | 99.990 % | 156 (93%)
conv6 | 56 x 56 x 256 | 3 | 56 x 56 x 256 | 100 % | 100 % | 99.995 % | 156 (93%)
conv7 | 56 x 56 x 256 | 3 | 56 x 56 x 256 | 100 % | 100 % | 99.995 % | 156 (93%)
conv8 | 28 x 28 x 256 | 3 | 28 x 28 x 512 | 100 % | 100 % | 99.990 % | 168 (100%)
conv9 | 28 x 28 x 512 | 3 | 28 x 28 x 512 | 100 % | 100 % | 99.995 % | 168 (100%)
conv10 | 28 x 28 x 512 | 3 | 28 x 28 x 512 | 100 % | 100 % | 99.995 % | 168 (100%)
conv11 | 14 x 14 x 512 | 3 | 14 x 14 x 512 | 100 % | 100 % | 99.982 % | 168 (100%)
conv12 | 14 x 14 x 512 | 3 | 14 x 14 x 512 | 100 % | 100 % | 99.982 % | 168 (100%)
conv13 | 14 x 14 x 512 | 3 | 14 x 14 x 512 | 100 % | 100 % | 99.982 % | 168 (100%)
100 % | 100 % | 98.928 % | 96.23 %

## Slide 56: PEs’ utilization rate of AlexNet
AlexNet | Model parameter |  |  | Utilization rate of 32 PEs | Utilization rate of 288 multipliers | 2D PE- Utilization rate of 32x32 PEs | Eyeriss Num. of active PEs
 | Input map | Kernel size | Output map |  |  |  | 
conv1 | 227 x 227 x 3 | 11 | 55 x 55 x 96 | 100 % | 96.03 % | 70.542 % | 154 (92%)
conv2 | 31 x 31 x 48 | 5 | 27 x 27 x 256 | 100 % | 92.6 % | 99.957 % | 135 (80%)
conv3 | 15 x 15 x 256 | 3 | 13 x 13 x 384 | 100 % | 100 % | 99.943 % | 156 (93%)
conv4 | 15 x 15 x 192 | 3 | 13 x 13 x 384 | 100 % | 100 % | 99.924 % | 156 (93%)
conv5 | 15 x 15 x 192 | 3 | 13 x 13 x 256 | 100 % | 100 % | 99.886 % | 156 (93%)
100 % | 97.726 % | 94.050 % | 90.2 %

## Slide 57: Convolution, Bias Addition, and ReLU PE Core
Convolution, bias ,and ReLU in PE

## Slide 58: Advanced DL Accelerator Version
1D PE Array Accelerator
  2021 US Provisional patent application (processing)
    Methods and Devices of Deep Learning and Inference Acceleration
  Micro-architecture
    Accelerator and PE micro-architecture
    Floating point data type (V1)
    Int-8-16-8 data type (V2)
  IPW data reuse scheme
    IPW reuses the Input feature map, Partial sum, and Weight to maximize the performance and efficiency.
  Computational data flow integration
    Conv, DW Conv, Activation, Pooling, FC, Re-quantization (output 8 bits) in PE (V2)
  Different kernel size mapping
  Data placement strategy for different input map size
  1x1 kernel optimization
64x64 tile

## Slide 59: Memory System
Data fetcher and data placement is as critical as the MAC PE micro-architecture
Memory bandwidth requirement
  In an SoC system, accelerator may not get the use of the DRAM memory right away.
Use DMA operation scheduling to hide the DRAM memory access latency
DRAM
Memory
bus
Accelerator
SRAM
DMA controller
Intelligent fetcher
Arbiter

## Slide 60: Kneron Example: Larger kernel, geometric directly mapping on 3x3 PEs

## Slide 61: Kneron Patent
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x
x

## Slide 62: Thank You
Machine Learning
Hello!! R2-D2