## Slide 1: 處理器設計與實作
NCKU CASLAB

## Slide 2: Lab3: The Usage of GNU Debugger
By 謝宛珊
CASLAB

## Slide 3: Purpose
- Be familiar with the usage of GNU debugger on the simulator
- Know how to debug a program

## Slide 4
Outline
- Introduction of GNU Debugger (gdb)
- gdb command
- The usage of gdb
- Example
- Practice

## Slide 5: Introduction of GNU Debugger (1/4)
- Briefly call gdb
- A well-known and widespread open source debugger for software debugging within GNU POSIX development environment
- Can run on Unix-like systems and works for many languages (C, C++, Java…)
- gdb is originally concerned to debug only application programs running on an OS

## Slide 6: Introduction of GNU Debugger (2/4)
- debugged program usually runs on remote (target) machine, while gdb runs on host machine
- remote debugging protocol (RDP) is for host communicating with target program inside a remote machine (via TCP/IP network)

## Slide 7: Introduction of GNU Debugger (3/4)
- It is difficult to apply gdb to debug a bare-level program which might control and manage the system resources
- To debug bare-level program, use JTAG probe and ICE
- Joint Test Action Group (JTAG) for capturing signals on input/output ports
- In-circuit Emulator let programmers load programs into the system, run them, step through them

## Slide 8: Introduction of GNU Debugger (4/4)
Debugged program
gdb
(gdb)
What gdb can do:
- Let users set up a breakpoint in a program (usually the point where the
program fault)
- Let the program stop running when meets that breakpoint
- Print debug information, such as values in registers

## Slide 9
gdb command (1/2)
Look up a command :
    (gdb) help/ (gdb) help command
- Setting up breakpoints at a label :
(gdb) break label_name/ (gdb) b label_name
ex: (gdb) break main/ b main
- Setting up breakpoints at a particular address :
(gdb) break address/ (gdb) b address
ex: (gdb) break *0x0000ffff/ b *0x0000ffff
- Run the program and it will stop at a breakpoint or the end of the program:
(gdb) run
- Continue execution:
(gdb) continue/ (gdb) c

## Slide 10
gdb command (2/2)
- Execute one/ multiple instruction:
(gdb) stepi / (gdb) stepi 5
- Execute one instruction like stepi, but proceed through function calls:
(gdb) nexti
- Look at the contents of registers:
(gdb) info reg
- Look at the contents of memory:
(gdb) x/(nfu) address
(optional) n: number of display items, f: format, u: size of items
ex: (gdb) x/x 0x1010000
(gdb) x/1xw 0x1010000

## Slide 11
a. put the debugged program (name it test.c)in ~/mvp-NCKU/prog/test/
b. go to ~/mvp-NCKU/prog/
c. [~/mvp-NCKU/prog]$ make
d. go to ~/mvp-NCKU/
The usage of gdb
make gdb connection on host machine (1/2)

## Slide 12
e. [~/mvp-NCKU]$ ./run vpdg port_number
(if it fails, try ./run vpg port_number)
ex: ./run vpdg 8888
The usage of gdb
make gdb connection on host machine (2/2)

## Slide 13
a. go to ~/mvp-NCKU/prog
b. [~/mvp-NCKU/prog]$ ./mvpgdb port_name
ex: ./mvpgdb 8888
Debugged program
gdb
The usage of gdb
make gdb connection on target machine

## Slide 14
a. set the breakpoint
ex: (gdb) b main
The usage of gdb
start debugging – run program (1/2)

## Slide 15
b. run the program
ex: (gdb) c
The usage of gdb
start debugging – run program (2/2)

## Slide 16
c. dump the values in registers
ex: (gdb) info reg
The usage of gdb
start debugging – view information

## Slide 17
a. (gdb) q
The usage of gdb
start debugging – quit gdb

## Slide 18: Example (1/4)
Let’s look at the first lab we’ve done in MIPS CPU
pseudo code:
i uses $8, sum uses $9
for (i = 1; i<=10; i++)
sum = sum + i
Part of ARM assembly code

## Slide 19: Example (2/4)
Step 1: make gdb connection
In ~/mvp-NCKU
In ~/mvp-NCKU/prog

## Slide 20: Example (3/4)
Step 2: set breakpoint, then run
Breakpoint at main
pc is at 0x2194 (which is the first line in main )
ARM assembly code

## Slide 21: Example (4/4)
Finish first iteration
Finish first iteration
r8, r9 now store 1
Keep executing 7 instructions
Now pc is at 0x21b0 (ble 21a4 <loop>)
ARM assembly code

## Slide 22
Practice 1 (1/2)
- Goal:
Find the right numbers
- Description:
First look at test.s(test.txt). Then use gdb to find out the numbers stored in test.s(test.txt).
There are five numbers, to check if the ones you found are correct, use ./test_gdb.o X X X X X(X in decimal format), it will tell you if every number matches the correct one

## Slide 23
Practice 1 (2/2)
- Hint:
This program does calculation of a series of numbers, then stores the result back to memory.
- Notice:
Put test.txt, test.o, test.elf in /mvp-NCKU/prog/, then start debugging
Put test_gdb.o outside mvp-NCKU, then use ./test_gdb.o X X X X X
- Report Requirement:
Describe how do you use gdb to find the numbers.
Show the numbers you found.

## Slide 24: Practice2 (1/2)
- Goal:
Debug a program
- Description:
What this program does is sorting numbers in ascending order, however,
there are some bugs in the program, which make it behave incorrectly.
Uses gdb to debug and then modify the program (.s file)
so that it will sort numbers in ascending order.

## Slide 25: Practice2 (2/2)
- Notice:
There are 1 file in folder gdb_practice2:
test.s (bug program)
Follow the steps in Lab2 to produce test.elf for this test.s,
then follow the usage of gdb to debug the program.
- Report Requirement:
Describe how do you use gdb to debug this program.

## Slide 26: 實驗結報
結報格式(每組一份)
  封面
  實驗內容(程式碼註解、結果截圖)
  實驗心得
繳交位置
  ftp : //140.116.164.252
  帳號 / 密碼 : computer_arch_lab / co2014
DeadLine: Sun. PM11:59
TA Contact Information:
  助教信箱 : q36034099@mail.ncku.edu.tw
  Rm 92617
  Office hour : (Monday)10:00am~12:00pm