## Slide 1: Supplement on Verilog FF circuit examples
Based on
Fundamentals of Digital Logic with Verilog Design, Fundamentals of Logic Design, and MIT slides
Chung-Ho Chen

## Slide 2: A Gated D Latch
module D_latch (D, Clk, Q);
input D, Clk;
output reg Q;
always @(D, Clk)
if (Clk)
Q = D;
endmodule
Clk
Clk
Q = D if Clk = 1, the Verilog compiler assumes that
the value of Q caused by the if must be
maintained when Clk is not equal to 1.
This implies that a memory, a latch is instantiated.
Whenever D or Clk
changes, Q changes.
Not a real register!!
A Verilog register
needed because of
assignment in always block

## Slide 3: A D Flip-Flop
posedge
module flipflop (D, Clk, Q);
input D, Clk;
output reg Q;
always @(posedge Clk)
Q = D;
endmodule
negedge

## Slide 4: Blocking assignment: evaluation and assignment are immediate
Blocking assignment:
always @ (a or b or c)
begin
x = a | b; 1. evaluate a | b, and assign result to x
y = a ^ b ^ c; 2. evaluate a ^ b^c, and assign result to y
end

## Slide 5: Non-Blocking assignment
Nonblocking assignment: all assignments deferred until all right-hand sides have been evaluated (end of simulation timestep)
always @ (a or b or c)
begin
x <= a | b; 1. evaluate a | b, but defer assignment of x
y <= a ^ b ^ c; 2. evaluate a ^ b^c, but defer assignment of y
end 3. assign x, y with their new values
Non-blocking assignment is 2-step processes:
  Step 1: Evaluate the RHS
  Step 2: Update the LHS
Sometimes, as above, blocking and non-blocking produce the same result.
Sometimes, not!

## Slide 6: Why two ways of assigning values?

## Slide 7: Use blocking assignment for combinational always blocks
always @ (input a, b, c, output reg x, y)
begin
x = a & b;
y = x | c;
end
always @ (input a, b, c, output reg x, y)
begin
x <= a & b;
y <= x | c;
end
This is incorrect!
a b c x y
1 1 0 1 1
0 1 0 1 1
0 1 0 1 1 x<=0, new value for x is 0, but not assigned yet.
0 1 0 1 1 x<=0, y <=1
0 1 0 0 1 assignment completion
Non-Blocking behavior
Initial condition
a changes; always block triggered
x = a & b;
y = x | c;

## Slide 8: Verilog Simulation Behavior
Always blocks and “assign” statements execute in parallel
  Signals in the sensitivity list (@(..)) trigger the always blocks.
  “assign” triggered when RHS signal changes.
All non-blocking assignment statements in an always block are evaluated using the values that the variables have when the always block is entered.
  That is, a given variable has the same value for all statements in the block.
  The result of each non-blocking assignment is not seen until the end of the always block.

## Slide 9: Blocking Assignment
module two-FFs (D, Clock, Q1, Q2);
input D, Clock;
output reg Q1, Q2;
always @(posedge Clock)
begin
Q1 = D;
Q2 = Q1;
end
endmodule
// blocking assignment here, so at each rising clock edge,
Q1=D, after that, Q2 = Q1, finally Q2=Q1=D
This implies a circuit below:

## Slide 10: Non-Blocking Assignment
module two-FFs (D, Clock, Q1, Q2);
input D, Clock;
output reg Q1, Q2;
always @(posedge Clock)
begin
Q1 <= D;
Q2 <= Q1;
end
// at the end of always block, Q1 and Q2
change to a new value concurrently.
endmodule
// at the rising clock edge,
Q1 and Q2 simultaneously receive the old values of D, and Q1.

## Slide 11: D-FF with Asynchronous Reset (Clear)
module flipflop (D, Clock, ClrN, Q);
input D, Clock, ClrN;
output reg Q;
always @(negedge ClrN, posedge Clock)
if (!ClrN) // if clear, then,
Q <= 0;
else // normal update
Q <= D;
endmodule
What about both? PreN and ClrN

## Slide 12: D-FF with Synchronous Reset
module flipflop (D, Clock, ClrN, Q);
input D, Clock, ClrN;
output reg Q;
always @(posedge Clock)
if (!ClrN) // if clear, then,
Q <= 0;
else // normal update
Q <= D;
endmodule
What about both? PreN and ClrN

## Slide 13: n-bit register
Naming: Resetn
16 bits here
Asynchronous clear
module regn (D, Clock, Resetn, Q);
parameter n = 16;
input [n-1:0] D;
input Clock, Resetn;
output reg [n-1:0] Q;
always @(negedge Resetn, posedge Clock)
if (!Resetn)
Q <= 0;
else
Q <= D;
endmodule

## Slide 14: Shift Register
L: load register with input.
Non-blocking statements, so that value before clock edge is shifted into the destination bit, at the end of the always block.
module shift4 (R, L, Din, Clock, Q);
input [3:0] R;
input L, Din, Clock;
output reg [3:0] Q;
always @(posedge Clock)
if (L)
Q <= R;
else
begin
Q[0] <= Q[1];
Q[1] <= Q[2];
Q[2] <= Q[3];
Q[3] <= Din;
end
endmodule
DFF 2
Q2
DFF 3
D
Q3
DFF 0
Q1
Din
DFF 3
Q0

## Slide 15: Up Counter with enable
If not reset, at rising edge and enabled, increment the counter by 1
module upcount (Resetn, Clock, E, Q);
input Resetn, Clock, E;
output reg [3:0] Q;
always @(negedge Resetn, posedge Clock)
if (!Resetn)
Q <= 0;
else if (E)
Q <= Q + 1;
endmodule

## Slide 16: Up/down Counter with enable
Q <= Q+1
Q <= Q-1
module UDcount (R, Clock, L, E, up_down, Q);
parameter n = 8;
input [n-1:0] R;
input Clock, L, E, up_down;
output reg [n-1:0] Q;
always @(posedge Clock)
if (L)
Q <= R;
else if (E)
Q <= Q + (up_down ? 1 : -1);
endmodule

## Slide 17: FF with an enable
module rege (D, Clock, Resetn, E, Q);
input D, Clock, Resetn, E;
output reg Q;
always @(posedge Clock, negedge Resetn)
if (Resetn == 0)
Q <= 0;
else if (E)
Q <= D;
endmodule